Shuttering Magnet

With this Magnet, wooden or steel formworks can be safely fixed to Steel 
moulds or Tables. The product is delivered with integrated high-prefomance magnets 
with forces from 450 to 2100 kg. Integrated threads (M16) can be used to adapt 
special formwork constructions to the Boxes. When the magnets are activated, steel 
springs are pulling the fromwork againsed the basic steel plate 

Advantages / Overview: 
– High Forces from 450 to 2100 kg 
– Integrated automatic mechanism with steel springs 
– Integrated threads M16 to adapt formwork 
– Same magnet can be used for different purposes 
– Adapters for your demand can be delivered on request

Specifications:

2100kgs &1800kgs

L= 320mm
B= 120mm
H1= 60mm (Box)
H2= 84mm (Magnet Activated)
H3= 94mm (Magnet Deactivated)

900kgs

L= 280mm
B= 60mm
H1= 40mm (Box)
H2= 69mm (Magnet Activated)
H3= 79mm (Magnet Deactivated)

450kgs

L= 170mm
B= 60mm
H1= 40mm (Box)
H2= 69mm (Magnet Activated)
H3= 79mm (Magnet Deactivated)