| HONGER PRESS FEEDERS |
| --- |
| 1. RNC Servo Feeder for material thickness 0.2-3.2mm |  |  |  |  |
| Model | RNC-200 | RNC-300 | RNC-400 | RNC-500 | RNC-600 | RNC-700 | RNC-800 |
| Coil Width (mm) | 200 | 300 | 400 | 500 | 600 | 700 | 800 |
| Feeding Length (mm) | 9999.99 |
| Coil Thickness (mm) | 0.2-3.2 |
| Releasing System | Pneumatic Type |
| Feeding Roller (mm) | Top Ø65, Bottom Ø80 |
| Feeding Speed (m/min) | 20 |
| Power (kW) | 0.85 | 1.3 | 1.8 | 1.8 | 2.9 | 2.9 | 2.9 |
| Servo Motor | Yaskawa, Japan |
| Servo Drives | Yaskawa, Japan |
| PLC | Mitsubishi, Japan |
| Touch Screen | Weinview, Taiwan |
| Feeding Accuracy | ±0.1mm |
| 2. RNC-B Servo Feeder for material thickness 0.5-4.5mm |  |  |  |  |
| Model | RNC-300B | RNC-400B | RNC-500B | RNC-600B | RNC-700B | RNC-800B |  |
| Coil Width (mm) | 300 | 400 | 500 | 600 | 700 | 800 |  |
| Feeding Length (mm) | 9999.99 |  |
| Coil Thickness (mm) | 0.5-4.5 |  |
| Releasing System | Pneumatic Type |  |
| Feeding Roller (mm) | Top Ø75, Bottom Ø90 |  |
| Feeding Speed (m/min) | 20 |  |
| Power (kW) | 1.3 | 1.8 | 2.9 | 2.9 | 4.4 | 4.4 |  |
| Servo Motor | Yaskawa, Japan |  |
| Servo Drives | Yaskawa, Japan |  |
| PLC | Mitsubishi, Japan |  |
| Touch Screen | Weinview, Taiwan |  |
| Feeding Accuracy | ±0.1mm |  |
| 3. RNC-H Servo Feeder for material thickness 0.5-6.0mm |  |  |  |
| Model | RNC-300H | RNC-400H | RNC-500H | RNC-600H |  |  |  |
| Coil Width (mm) | 300 | 400 | 500 | 600 |  |  |  |
| Feeding Length (mm) | 9999.99 |  |  |  |
| Coil Thickness (mm) | 0.5-6.0 |  |  |  |
| Releasing System | Pneumatic Type |  |  |  |
| Feeding Roller (mm) | Top Ø90, Bottom Ø90 |  |  |  |
| Feeding Speed (m/min) | 20 |  |  |  |
| Power (kW) | 1.8 | 2.9 | 2.9 | 4.4 |  |  |  |
| Servo Motor | Yaskawa, Japan |  |  |  |
| Servo Drives | Yaskawa, Japan |  |  |  |
| PLC | Mitsubishi, Japan |  |  |  |
| Touch Screen | Weinview, Taiwan |  |  |  |
| Feeding Accuracy | ±0.1mm |  |  |  |
| 4. NCF Servo Feeder with mechanical release |  |  |  |  |  |
| Model | NCF-100 | NCF-200 | NCF-300 | NCF-400 |  |  |  |
| Coil Width (mm) | 100 | 200 | 300 | 400 |  |  |  |
| Feeding Length (mm) | 9999.99 |  |  |  |
| Coil Thickness (mm) | 0.1-1.6 |  |  |  |
| Releasing System | Mechanical Release |  |  |  |
| Feeding Roller (mm) | Top Ø65, Bottom Ø80 |  |  |  |
| Feeding Speed (m/min) | 20 |  |  |  |
| Power (kW) | 0.85 | 0.85 | 1.3 | 1.8 |  |  |  |
| Servo Motor | Yaskawa, Japan |  |  |  |
| Servo Drives | Yaskawa, Japan |  |  |  |
| PLC | Mitsubishi, Japan |  |  |  |
| Touch Screen | Weinview, Taiwan |  |  |  |
| Feeding Accuracy | ±0.1mm |  |  |  |
| 5. RF Mechanical Roll Feeder |  |  |  |  |  |  |
| Model | RF-105NS | RF-205NS | RF-305NS | RF-405NS | RF-138NS |  |  |
| Coil Width (mm) | 100 | 200 | 300 | 400 | 130 |  |  |
| Feeding Length (mm) | 50 | 50 | 50 | 50 | 80 |  |  |
| Coil Thickness (mm) | 0.1-1.6 |  |  |
| Mould Line Height (mm) | 55-100 | 60-120 |  |  |
| Model | RF-1310NS | RF-2010NS | RF-3010NS | RF-4010NS | RF-2015NS |  |  |
| Coil Width (mm) | 130 | 200 | 300 | 400 | 200 |  |  |
| Feeding Length (mm) | 100 | 100 | 100 | 100 | 150 |  |  |
| Coil Thickness (mm) | 0.1-3.5 |  |  |
| Mould Line Height (mm) | 70-140 |  |  |
| Model | RF-3015NS | RF-4015NS | RF-1320NS | RF-2020NS | RF-3020NS | RF-4020NS |  |
| Coil Width (mm) | 300 | 400 | 130 | 200 | 300 | 400 |  |
| Feeding Length (mm) | 150 | 150 | 200 | 200 | 200 | 200 |  |
| Coil Thickness (mm) | 0.1-3.5 |  |
| Mould Line Height (mm) | 70-140 |  |
| 6. GS High Speed Gripper Feeder |  |  |  |  |  |  |
| Model | GS-906 | GS-1512N | NRG-80 |  |  |  |  |
| Coil Width (mm) | 0-90 | 0-150 | 8-80 |  |  |  |  |
| Max. Feeding Length | 60 | 120 | 80 |  |  |  |  |
| Feeding Angle | 180 | 165 |  |  |  |  |
| Coil Thickness (mm) | 0.1-1.5 | 0.1-2.0 |  |  |  |  |
| Feeding Line Height | 60-120 |  |  |  |  |
| Release Angle | Adjustable |  |  |  |  |
| Feeding Mechanism | Crank Shaft Transmission |  |  |  |  |
| Installation Location | Left |  |  |  |  |
| Feeding Direction | L→R |  |  |  |  |
| 7. GCF High Speed Cam Feeder |  |  |  |  |  |  |
| Model | CGF-150 | GCF-200 | GCF-300 |  |  |  |  |
| Coil Width (mm) | 150 | 200 | 300 |  |  |  |  |
| Coil Thickness (mm) | 0.1-1.6 |  |  |  |  |
| Index No. | 4 |  |  |  |  |
| Feeding Length (mm) | 11.5-240 |  |  |  |  |
| Feeding Angle | 180 |  |  |  |  |
| Release Angle | 135-195 |  |  |  |  |
| Feeding Direction | L→R |  |  |  |  |
| 8. Air Feeder |  |  |  |  |  |  |  |
| Model | AF-1C | AF-2C | AF-3C | AF-4C | AF-5C | AF-6C |  |
| Coil Width (mm) | 50 | 65 | 80 | 100 | 150 | 200 |  |
| Feeding Length (mm) | 50 | 80 | 80 | 130 | 150 | 200 |  |
| Coil Thickness (mm) | 0.1-0.5 | 0.1-0.8 | 0.1-1.2 | 0.1-1.5 | 0.1-2.0 | 0.1-2.0 |  |
| Feeding Speed (m/min) | 12 |  |
| Air Consumption (L/mm) | 26.5 | 38.5 | 47 | 58.6 | 100.5 | 108.5 |  |
| Pneumatic Pressure (kg/cm²) | 4.5 |  |
| Model | AF-7C | AF-8C | AF-9C | AF-10C | AF-12C |  |  |
| Coil Width (mm) | 250 | 300 | 350 | 400 | 500 |  |  |
| Feeding Length (mm) | 250 | 300 | 350 | 400 | 500 |  |  |
| Coil Thickness (mm) | 0.1-2.5 | 0.1-2.5 | 0.1-3.0 | 0.1-3.0 | 0.1-3.0 |  |  |
| Feeding Speed (m/min) | 12 |  |  |
| Air Consumption (L/mm) | 152 | 162.5 | 172 | 182.5 | 195 |  |  |
| Pneumatic Pressure (kg/cm²) | 4.5 |  |  |
| Please contact with our sales team to find a suitable configuration for your material: |  |  |  |
| Email: export@he-machine.com |  |  |  |  |  |  |
| Tel: +86 755 28372363 |  |  |  |  |  |  |  |
| Add: F1601-02, A4 Bldg Zhujiang Plaza, Longgang, Shenzhen, 518172, China |  |  |  |
| www.hongerjixie.com |  |  |  |  |  |  |  |