1.Product name: Standard uncoiler machine ,Model:MT

1.Feature and advantage:

- It can work together with straighener. Buyer can also choose non motive power style

- Maximum load weight is 2 ton.

- Maximum material width is 800mm.Suitable for all kinds of metal coil automatic uncoilling ,easy to operate.

- Suitable for metal parts, electron, electrical appliance, toy and auto parts continuous pressing production.

- The cheapest price machine ,High quality ,lowest maintenance.

- We can customize the machine.

- Fast speed:0-16m/min.

- Coil car , pressing arm ,hydraulic expansion etc. for choosing.

2.Introduction

- Shenzhen Honger Machine Equipment Co.,Ltd are professional Uncoiler Sraightener 2 in 1 Machine,Uncoiler machine ,straightener machine ,servo feeder machine ,high speed press machine etc. in China.We are the only own international advanced big CNC that include FPW & VMC.The best quality best price Uncoiler Machine manufacturer in Guangdong.

- Our Uncoiler Machine speed can reach 0-16m/min. And suitable 0-800mm width all kinds of metal coil opening.

- Our Uncoiler Machine is suitable all metal coil opening.

- Our Uncoiler Machine widely used to computer, mobile phone,automobile industry,appliances manufacturing, medical apparatus and instruments, hardware & Metal parts etc industry.

- Technical data:

| Name | Standard Uncoiler/Decoiler machine |
| --- | --- |
| Model | MT-200 | MT-300 | MT-400 | MT-500 | MT-600 | MT-800 |
| Max.Coil width | 200mm | 300mm | 400mm | 500mm | 600mm | 800mm |
| Coil thickness | 0.35-1.6mm |
| Coil I.D. | 450-530mm |
| Coil O.D. | 1200mm |
| Coil weight | 500kg | 800kg | 1000kg | 1500kg | 2000kg | 2000kg |

- Buyer requirement:

| Package | Wooden case |
| --- | --- |
| After-Sale service | 1 Year |
| Delivery time | 0-10workdays |
| Shipping way | Ocean shipping |
| Payment term | T/T L/C Cash or other |

- Product attribute

| CE Certificate | Passed |
| --- | --- |
| Coil width | 0-800mm |
| Stock | With |
| Expansion way | Manual or hydraulic |
| Big customer | Media, Haier , AUDI,DONGFENG etc. |

- Matched equipment

- Progressive Mould/tool/die

- Beg heavy press machine

- Photoelectric hand

- Automatic feeder machine

- Conveyer belt etc.

8.Finished product showing: