1.Product name: Non-tandard uncoiler machine ,Model:MT-F

2.Introduction

- Shenzhen Honger Machine Equipment Co.,Ltd are professional Uncoiler Sraightener 2 in 1 Machine,Uncoiler machine ,straightener machine ,servo feeder machine ,high speed press machine etc. in China.We are the only own international advanced big CNC that include FPW & VMC.The best quality best price Uncoiler Machine manufacturer in Guangdong.

- Our Uncoiler Machine speed can reach 0-16m/min. And suitable 600-2000mm width all kinds of metal coil opening.

- Our Uncoiler Machine is suitable all metal coil opening.

- Our Uncoiler Machine widely used to computer, mobile phone,automobile industry,appliances manufacturing, medical apparatus and instruments, hardware & Metal parts etc industry.

- Feature and advantage:

- It can work together with straighener. Buyer can also choose non motive power style

- Maximum load weight is 20 ton.

- Maximum material width is 2000mm.Suitable for all kinds of metal coil automatic uncoilling ,easy to operate.

- Suitable for metal parts, electron, electrical appliance, toy and auto parts continuous pressing production.

- The cheapest price machine ,High quality ,lowest maintenance.

- We can customize the machine.

- Fast speed:0-16m/min.

- Coil car , pressing arm ,hydraulic expansion etc. for choosing.

- Technical data:

| Model | unit | MT-600F | MT-800F | MT-1000F | MT-1300F |
| --- | --- | --- | --- | --- | --- |
| Material width | mm | 600 | 800 | 1000 | 1300 |
| Material thickness | mm | 0.35-1.6 | 0.35-1.6 | 0.35-1.6 | 0.35-1.6 |
| Max.outer dia | mm | 1200 | 1200 | 1200 | 1200 |
| Material inner dia | mm | Ø450-530 | Ø450-530 | Ø450-530 | Ø450-530 |
| Material weight | kg | 5000 | 5000 | 8000 | 10000 |
| Expansion way | Hydraulic expansion |

- Buyer requirement:

| Package | Wooden case |
| --- | --- |
| After-Sale service | 1 Year |
| Delivery time | 0-10workdays |
| Shipping way | Ocean shipping |
| Payment term | T/T L/C Cash or other |

- Product attribute

| CE Certificate | Passed |
| --- | --- |
| Coil width | 600-2000mm |
| Coil weight | 0-20Ton |
| Expansion way | Manual or hydraulic |
| Big customer | Media, Haier , AUDI,DONGFENG etc. |

- Matched equipment

- Progressive Mould/tool/die

- Beg heavy press machine

- Photoelectric hand

- Automatic feeder machine

- Conveyer belt etc.

8.Finished product showing: