New KingFast Technology

C-Drive Series

KF2710MCS19 SATA Solid State Drive Datasheet

（Based on NAND Flash）

Version: 1.1

May , 2014

NOTE: INFORMATION IN THIS PRODUCT SPECIFICATION IS SUBJECT TO CHANGE AT ANYTIME WITHOUT NOTICE.

ALL PRODUCT SPECIFICATIONS ARE PROVIDED FOR REFERENCE ONLY.TO ANY INTELLECTUAL PROPERTY

RIGHTS IN NEW KINGFAST PRODUCT OR TECHNOLOGY.ALL INFORMATION IN THIS DOCUMENT IS PROVIDED.

Table of contents

New KingFast Technology	1

C-Drive Series	1

KF2710MCS19 SATA Solid State Drive Datasheet	1

I.	Introduction	3

1 Overview	3

2 Part Type Introduction	3

Outline	4

II.	Block Diagram	5

IV. Product Specifications	6

4.1 Physical Dimensions	6

4.2 Interface Specification	7

4.2.1 Pin Assignment	7

4.2.2 Interface Mode	7

V. Reliability	8

5.1 ECC Descriptions	8

5.2 Advance Wear-Leveling Algorithm	8

5.3 S.M.A.R.T Function	8

VI. Ordering Information	9

VII. Related documentation	9

Attachment	9

# Introduction

## 1 Overview

KingFast SATA SSD (Solid State Drive) is a high performance and high reliability storage device based on NAND Flash technology that designed to solve the bottleneck of computing system by traditional hard disk drives. Our SATA SSD doesn't have a moving parts and it has a same host interface and same physical dimension with Hard Disk Drive, so it can be drop-in replaced with the hard disk drives without anything. With a high performance and low power consumption, Our SATA SSD can be a good storage device for NB and Tabletop PC.

KingFast SATA SSD purely consists of semiconductor devices and NAND flash memories, which give rugged features against shock and vibration, used in extreme environment such as industrial PC to increase MTBF. Furthermore, Our SATA SSD has highly advanced flash memory management algorithm to guarantee higher performance and data integrity.

## 2 Part Type Introduction

This chapter is about the specifications of the 2.5” SATA Solid State Drive SSD with SATAⅡ interface.

| Type | Capacity | Flash | Interface |
| --- | --- | --- | --- |
| KF2710MCS19 | 128GB | MLC | SATAIII |
|  | 256GB | MLC | SATAIII |

Table 1 Capacity Specifications

| Capacity | Available Capacity | R / W(MB/s) | Random R/W IOPS |
| --- | --- | --- | --- |
| 128GB | 118GB | 560/460 | 60000 / 30000 |
| 256GB | 236GB | 560/460 | 70000 / 40000 |

Note: the maximum Read & Write performance test with ATTO Disk Benchmark;

IOPS test with IOmeter 2008.

# Outline

| Based spec | Interface | SATAIII |
| --- | --- | --- |
|  | Dimension | 100*70*7 mm |
|  | Weight① | 62~72 g |
|  | Capacity | 128GB~256GB |
|  | SDram | 256MB |
|  | Flash type | MLC NAND Flash |
| Read/Write Performance② | Sequential Read | Up to 560MB/s |
|  | Sequential Write | Up to 460MB/s |
|  | 4KB Random Read IOPS | 70000 |
|  | 4KB Random Write IOPS | 70000 |
|  | Response Time | 0.2ms |
| Power Consumption | Power Supply | 5V+5% |
|  | Standby | 0.3W |
|  | Maximum Ripple | 70 mV(peak to peak) |
|  | 4KB Random Write | 2.5W |
| Reliability | Write endurance: 8 years @ 100G write/day(32G) |
|  | Read endurance: unlimited |
|  | MTBF: >2,000,000 hours |
|  | Data retention: >20years @ 25℃ |
|  | Data destroy do not support |
|  | Sudden power-off recovery support |
|  | S.M.A.R.T,NCQ,Trim and dynamic power management support |
|  | Static and dynamic wear-leveling |
|  | Bad block management algorithm |
|  | ECC: Supports BCH ECC 66 bits in 1024 bytes |
| Environment | Storage temperature: -55~95 ℃ |
|  | Operation temperature: -0~75℃ |
|  | Humidity: 5%~95% |
|  | Vibration | 15G (10 to 2000Hz) |
|  | Shock | 350G at 0.5ms |
| Warranty | 3 years |

Table 2 outline of the driver

①, ②: The Read/Write performance and weight vary with different capacity of products.

The testing environment is below:

OS: Windows 7 Ultimate

CPU: Intel (R) Core(TM) i3-2100T CPU @2.50GHz

Memory: 4GB

Motherboard: Asrock H67M

Test program: ATTOBenchMark V2.47 (sequential R/W speed)

IOmeter2008 (IOPS)

HD tune V4.6.1 (sustainably R/W speed, access time)

Test Drive: KF2710MCS19-128GB (MLC)

# Block Diagram

Figure 2   Block Diagram

# IV. Product Specifications

## 4.1 Physical Dimensions

| Parameter | Value |
| --- | --- |
| Length | 100+0.1 mm |
| width | 70+0.1 mm |
| height | 7+0.1 mm |

Table 3 Physical dimensions of the driver

Figure 3 Physical dimensions

## 4.2 Interface Specification

### 4.2.1 Pin Assignment

Figure 4 Pin connector

| Pin number | Signal name | Description |
| --- | --- | --- |
| S1 | GND | 2nd mate |
| S2 | A+ | Differential signal pair A From physical layer electronics |
| S3 | A- |  |
| S4 | GND | 2nd mate |
| S5 | B- | Differential signal pair B From physical layer electronics |
| S6 | B+ |  |
| S7 | GND | 2nd mate |
| P1 | V33 | 3.3V power (unused) |
| P2 | V33 | 3.3V power (unused) |
| P3 | V33 | 3.3V power,pre-charge,2nd mate(unused) |
| P4 | GND | 1st mate |
| P5 | GND | 2nd mate |
| P6 | GND | 2nd mate |
| P7 | V5 | 5V power,pre-charge,2nd mate |
| P8 | V5 | 5V power |
| P9 | V5 | 5V power |
| P10 | GND | 2nd mate |
| P11 | DAS/DSS | Device activity signal/Disable staggered spinal(unused) |
| P12 | GND | 1st mate |
| P13 | V12 | 12V power,pre-charge,2nd mate(unused) |
| P14 | V12 | 12V power(unused) |
| P15 | V12 | 12V power(unused) |

Table 4  SATAⅡ interface pin assignment

### 4.2.2 Interface Mode

The interface of the 2.5” SATA SSD complies with the standard Serial ATA version 3.1:

- Host Transfer Rate is 600MB/s(6.0Gb/s)

- PIO mode 0,1,2,3,4

- DMA mode 0,1,2

- UDMA mode 0,1,2,3,4,5,6

# V. Reliability

### 5.1 ECC Descriptions

Please refer to FIG. 5 that is a diagram illustrating an allocating method of a spare area in each page of a NAND flash memory, where in the specific ECC algorithm utilizes a Bose, Chaudhuri and Hocquengham (BCH) ECC algorithm. When a BCH 16 ECC algorithm encodes the data in the NAND flash memory, the parity code generated in the encoding process may occupy 28 bytes of the spare area in each page. When a BCH 24 ECC algorithm encodes the data in the NAND flash memory, the parity code generated in the encoding process may occupy 42 bytes of the spare area in each page. When a BCH 16 algorithm decodes the data in the NAND flash memory, the data can be decoded correctly if the error bit happened in two sectors (1024Bytes) is 16. When a BCH 24 algorithm decodes the data in the NAND flash memory, the data can be decoded correctly if the error bit happened in two sectors is 24.

Figure 5 Allocation for ECC algorithm BCH in Nand Flash

### 5.2 Advance Wear-Leveling Algorithm

The NAND flash devices are limited by a certain number of write cycles. When using a file system, frequent file table updates is mandatory. If some area on the flash wears out faster than others, it would significantly reduce the lifetime of the whole device, even if the erase counts of others are far from the write cycle limit. Thus, if the write cycles can be distributed evenly across the media, the lifetime of the media can be prolonged significantly. The scheme is achieved both via buffer management and specific advanced wear leveling to ensure that the lifetime of the flash media can be increased, and the disk access performance is optimized as well.

### 5.3 S.M.A.R.T Function

S.M.A.R.T. is an acronym for Self-Monitoring, Analysis and Reporting Technology, an open standard allowing disk drives to automatically monitor their own health and report potential problems. It protects the user from unscheduled downtime by monitoring and storing critical drive performance and calibration parameters. Ideally, this should allow taking proactive actions to prevent impending drive failure. SMART feature adopts the standard SMART command B0h to read data from the drive. When the SMART Utility running on the host, it analyzes and reports the disk status to the host before the device is in critical condition.

# VI. Ordering Information

| Model | Capacity | PN |
| --- | --- | --- |
| KF2710MCS19 | 128GB | KF2710MCS19-128 |
| KF2710MCS19 | 256GB | KF2710MCS19-256 |

# VII. Related documentation

For more information, visit www.kfast.com.cn

# Attachment

Test platform：

System : Windows 7

CPU: Intel (R) Core(TM) i3-2100T CPU @2.50GHz

Memory : 4GB

Mother board: Asrock H67M

SSD：KF2710MCS19-128GB

Test performance  picture:

Crystaldiskmark

AS SSD benchmark: