| 风冷（低配）16-50mm |
| --- |
| 45/33 single screw extruder | Screw diameter: 45mm L/D Ratio: 33:1 Screw&barrel material: 38CrMoAlA Motor: 22kw Frequency inverter :DELTA Barrel heating method:Cast-alumium heating, with stainless steel protection Output: 50-80kg/h Temperature Control: Ormon Contactor: Dexili |
| Corrugated pipe forming machine | Motor: 2.2kw Frequency inverter: Delta Production speed:5m/min Quantity of shaping mould：60 pairs per set Cooling method:Air cooling |
| Single Winder | Inner diameter of coil(mm):can be made as your request Outside diamter of coil(mm):can be made as your request Working method: Manul |

Price:18280

| 风冷（中配）16-50mm |
| --- |
| 65/30 single screw extruder | Screw diameter: 65mm L/D Ratio: 30:1 Screw&barrel material: 38CrMoAlA Motor: 37kw Frequency inverter :DELTA Barrel heating method:Cast-alumium heating, with stainless steel protection Output:120-180kg/h Temperature Control: Ormon Contactor: Dexili |
| Corrugated pipe forming machine | Motor: 2.2kw Frequency inverter: Delta Production speed:8m/min Quantity of shaping mould：60 pairs per set Cooling method:Air cooling |
| Single Winder | Inner diameter of coil(mm):can be made as your request Outside diamter of coil(mm):can be made as your request Working method: Pneumatic |

Price:20650

| 风冷（高配）16-50mm PLC+4万 |
| --- |
| 65/30 single screw extruder | Screw diameter: 65mm L/D Ratio: 30:1 Screw&barrel material: 38CrMoAlA Motor: 37kw Barrel heating method:Cast-alumium heating, with stainless steel protection Output:120-180kg/h Temperature Control: Ormon Contactor: Dexili |
| Corrugated pipe forming machine | Motor: 2.2kw Frequency inverter: Delta Production speed:8m/min Quantity of shaping mould：60 pairs per set Cooling method:Air cooling |
| Single Winder | Inner diameter of coil(mm):can be made as your request Outside diamter of coil(mm):can be made as your request Working method: Pneumatic |

Price:20650

| 水冷（低配）16-50mm |
| --- |
| 65/33 single screw extruder | Screw diameter: 65mm L/D Ratio: 33:1 Screw&barrel material: 38CrMoAlA Motor: 45kw Frequency inverter :DELTA Barrel heating method:Cast-alumium heating, with stainless steel protection Output:130-200 kg/h Temperature Control: Ormon Contactor: Dexili |
| Corrugated pipe forming machine | Motor: 3kw Frequency inverter: ABB Production speed:20-25m/min Quantity of shaping mould：72 pairs per set Cooling method:Water cooling |
| Double Winder | Inner diameter of coil(mm):can be made as your request Outside diamter of coil(mm):can be made as your request Working method: Pneumatic |

Price:31140

| 水冷（中配）16-50mm |
| --- |
| 65/33 single screw extruder | Screw diameter: 65mm L/D Ratio: 33:1 Screw&barrel material: 38CrMoAlA Motor: 45kw Frequency inverter :DELTA Barrel heating method:Cast-alumium heating, with stainless steel protection Output:130-200 kg/h Temperature Control: Ormon Contactor: Dexili |
| Corrugated pipe forming machine | Motor: 3kw Frequency inverter: ABB Production speed:20-25m/min Quantity of shaping mould：72 pairs per set Cooling method:Water cooling |
| Ordinary Corrugated tube Cutting machine | Cutting length(mm):5-9999mm Cutting Width(mm):6-40mm Voltage/frequency:220/110V 50/60HZ Weight:65kg Diemension:700*580*450mm |

Price:29280

| 水冷（高配）16-50mm +PLC |
| --- |
| 65/33 single screw extruder | Screw diameter: 65mm L/D Ratio: 33:1 Screw&barrel material: 38CrMoAlA Motor: 45kw Frequency inverter :DELTA Barrel heating method:Cast-alumium heating, with stainless steel protection Output:130-200 kg/h Temperature Control: Ormon Contactor: Dexili |
| Corrugated pipe forming machine | Motor: 3kw Frequency inverter: ABB Production speed:20-25m/min Quantity of shaping mould：72 pairs per set Cooling method:Water cooling |
| Double Winder | Inner diameter of coil(mm):can be made as your request Outside diamter of coil(mm):can be made as your request Working method: pneumatic |

Price:37910