Dental Cone Beam Computed Tomography System(CBCT)

PLX3000A

PRESENTATION OF PRODUCT

# PERLOVE MEDICAL

Perlove Medical is a large scale and influential manufacturer of medical equipment in China. We are a group company with the overseas headquarter Nanjing Perlove in Eastern China. With years of development, Perlove Medical has found its typical corporate culture which is exactly embodied in the name of our headquarter company's name - Perlove.

★ Number of Employees: 1000(approx)

★ Area: 70,000 ㎡

★ Yearly Output Capacity ≥ 10000 sets

★ X-ray Range: Mobile, Stationary, DR, DRF, C-arm，Dental CBCT, etc.,

★ Mobile models with No. 1 market share in the past ten years

# PRODUCT DESCRIPTION

# Product Usage

# PLX3000A is a dental cone beam computed tomography system (CBCT), which is widely used for dental CT diagnosis and is mainly for oral and maxillofacial surgeries, orthognathic surgeries, such as tooth implantation, tooth extraction, root canal therapy, etc.

# Product Specification

| Item | Content | Technical Parameters |
| --- | --- | --- |
| Power | Voltage | 220V±10% |
|  | Frequency | 50Hz±1Hz |
| X-ray Generator | Power | 1.38KW |
|  | Tube voltage | 60kV—92kV |
|  | Tube current | 1mA—15mA |
| X ray tube | Tube Focus | 0.5mm |
|  | Anode thermal capacity | 35KJ(50KHU) |
|  | Information Display | KV, MA, Lifting position information, Laser lights indicate, body features |
| Digital Flat Penal Detector | Active area | 120(H)×100(V) |
|  | Pixel matrix | 1280(H)×1024(V) |
|  | Pixel pitch | 150 μm |
|  | Exposure time | 6S |
|  | Reconstruction time | ≤18s |
|  | A / D transition | 14 bit |
|  | Fluoroscopy Mode | Pulse Mode |
|  | Rotation | 200° |
|  | Scanning time | 18s |
| Mechanical Parameters | Information Display:KV, MA, Lifting position information, Laser lights indicate, body features |
|  | Vertical Movement Distance | 1000mm |
|  | Size | 788mm*1090mm*2200mm |
|  | Weight | 260kg |

# Product Advantages

- X-ray Source

★ Pulse Fluoroscopy Mode, low dose, green & safe.

- Flat Panel Detector

★ High resolution, small distortion, brightness uniformity.

★ Effective size:12cmx15cm

- Operating Interface

★ Touch Screen

★ Ergonomics Design

- High quality Panorama Image

★ CONE BEAM scanning three-dimensional imaging technology

★ 3D volumetric image could extract oral panorama with clear, low distortion & panoramic views.

- Networked device: high quality image and output information system

★ The networking functions of PLX3000A include: Dicom storage, Dicom film printing, Dicom film transfer.

★ It has standard DICOM 3.0 interface, supporting film printing, output, storage, barrier-free docking hospital PACS system.