WJ150-2200 -II type five layer corrugated board production line

WJ 150-2200-II型五层瓦楞纸板生产线

Equipment configuration and technical specification

设备配置及技术说明

已通过ISO：9001-2008标准质量管理体系认证

创新包装科技，打造一流品牌

| Hebei Dongguang Hengchuangli Carton Machinery Co., Ltd Company highway cangzhou county, hebei province Production line configuration list 生产线配置清单 |
| --- |
| Models规格型号 | Name 设备名称 | QTY 数量 | Unit price 单价 （万元） | Remark 备注 |
| ZJ-V5B | Hydraulic shaftless mill roll stand 全液压无轴 纸架 | 5台 （set） |  | Spindle ¢ 240mm, hyperbolic heavy rocker, expand chuck , multi-point brake, hydraulic drive lifting, panning left and right on the middle. 主轴￠240mm，双曲线重型摇臂，齿式夹纸头，多点式刹车,液压驱动升降，左右平移，对中等。 导轨长度6000mm，采用中板焊接。 |
|  | Rail and Tracks 上纸小车 | 10台 （set） |  | The guide track is 6000mm and the trolley is welded with 10mm。 导轨长度6000mm，小车采用10mm中板焊接。 |
| R06B | Pre-heater 面纸预热器 | 2台 （set） |  | Roller ￠600 mm, Pressure vessel certificate Electric adjustment package Angle.Angle can be adjusted within the range of 360 ° paper heated area. 辊筒￠600mm，含压力容器证书。电动调整包角。包角可在360°范围内调节纸张受热面积。 |
| R06B | Pre-heater 芯纸预热器 | 2台 （set） |  | Roller ￠600 mm, Pressure vessel certificate Electric adjustment package Angle.Angle can be adjusted within the range of 360 ° paper heated area. 辊筒￠600mm，含压力容器证书。电动调整包角。包角可在360°范围内调节纸张受热面积。 |
| SF-320C | Fingerless type single facer 单面瓦楞机 | 2台 （set） |  | Corrugated main roller ￠320mm，material with 48CrMo tungsten carbide dealing,Tile roll modular group lifting transfer.Airbag ballasting structure，import main bearing，PLC automatic control glue，HMI touch screen，Breaks automatic parking relief，steam heating way.瓦楞主辊￠320mm，材质采用48CrMo合金钢。瓦辊模块式成组吊换。气囊压载结构，进口主轴承，PLC自动控胶，人机界面触摸屏，断纸自动停车卸压，蒸气加热方式。 |
| RG-3-600 | Triple preheater 三重预热器 | 1台 （set） |  | Roller ￠600 mm, Pressure vessel certificate Electric adjustment package Angle.Angle can be adjusted within the range of 360 ° paper heated area. 辊筒￠600mm，含压力容器证书。电动调整包角。包角可在360°范围内调节纸张受热面积。 |
| GM-20 | Double glue machine 二层涂胶机 | 1台 （set） |  | The diameter of the roller is 269mm. Independent variable frequency motor drive, manual。 Adjustment of glue clearance. 涂胶辊直径269mm。独立变频电机驱动，手动调整涂胶间隙。 |
| ZDF | Conveyor bridge 输送过桥 | 1套 （set） |  | Adopt independent variable frequency motor drive, pull paper adsorption tensioning device. 采用独立变频电机驱动，牵纸吸附式张紧装置。 |
| SM-F | Double facer 双面机 | 1套 （set） |  | Rack 360 mm GB channel，Chrome hot plate 600 mm *12 pieces，control . Temperature display, frequency motor. 机架360 mm 国标槽钢，镀铬热板600 mm *12块，温度显示，变频电机。。 |
| ZQS | Thin knife slitting 薄刀分切机 | 1台 （set） |  | Electric thin knife, electric deflection , five-blade eight-wire, blade with tungsten alloy steel. 电动薄刀，电动调偏,五刀八线式,刀片用钨合金钢制作。 |
| NC-150 | NC cutter helical knives电脑螺旋刀横切机 | 1台 （set） |  | Ac servo control, energy storage brake, helical knife type structure, oil-immersed gear drive, 10.4-inch touch screen display. 全交流伺服控制，储能式制动，螺旋刀式结构，油浸式齿轮传动，10.4寸触摸屏显示。 |
| DM-XLM | Automatic small gantry stacking machine 全自动小龙门 堆码机 | 1台 （set） |  | Servo drive platform lifting, three-stage frequency conversion transport, automatic point stacking out, imported high-strength belt output, paper side standard delivery frame. 伺服驱动平台升降，三段变频输送，自动点数堆码排出，进口高强度皮带输出，岀纸侧标配输送架。 |
| ZJZ | Glue station system 制胶站系统 | 1套 （set） |  | The pipeline customer is prepared.The glue device is composed of carrier tank, main tank, storage tank, and glue pump and return pump. 管道客户自备。制胶装置分别有载体罐、主体罐、贮存罐、及送胶泵、回胶泵组成。 |
| QU | Air supply system 气源系统 | 1台 （set） |  | Customer's own gas source. 客户自备气源。 |
| ZQ | Steam system蒸汽系统 | 1套 （set） |  | Contain the valve of pipeline, steam trap,instrument and other steam components. 含设备内管道阀门、疏水阀、仪表等蒸汽元件，客户自备热源及管道。 |
| DQ | Electric control systems 电器控制柜系统 | 1套 （set） |  | Electric control system: single surface machine, drive part, double-sided machine, and glue applicator all adopt frequency conversion motor, Taiwan Delta variable frequency control system.The main relay adopts the French schneider famous brand products .电控系统：吸附式单面机、驱动部、双面机、涂胶机均采用变频电机，台达变频控制系统。主要继电器采用法国施耐德名牌产品。 |
| 合计 | Ex-factory price of RMB：（ price include tax） ￥： 人民币： （含税价） ￥： |
| Self-contained part 客户自备部分 1、Steam heating system：proposal with 4000Kg/Hr of a steam boiler pressure:1.25MPa steam pipeline。蒸汽供热系统：建议配4000Kg/Hr蒸汽锅炉一套， 压力为1.25Mpa，蒸汽管道。 2、Air compressed machine、air pipeline、glue conveying pipe。 空气压缩机、空气管道、胶液输送管道。 3、Power supply、wires connected to the operation panel and line pipe。 电源、电线接至操作柜及线路管道。 4、Water sources、water pipelines、buckets and so on。水源、输水管道、水桶等。 5、Water, electricity, gas flush mounting civil foundation。水、电、气地基平面安装土建工程。 6、Test with the base paper、corn starch (potato)、Industrial use caustic soda、borax and other material。试车用原纸、玉米（薯类）淀粉、工业用烧碱、硼砂等材料。 7、Oil equipment、lubricating oil、hydraulic oil、lubricating grease。 设备用机油、润滑油、液压油、润滑脂。 8、Installation、commissioning of food, accommodation。And provide installers with the installation.安装、调试人员的饮食、住宿。并提供安装工人配合安装。 |

※Main technical parameter and requirements

生产线主要技术参数及要求

Model: WJ150-2200 - Ⅱtype five layer corrugated board production line:

型号：WJ150-2200-Ⅱ型五层瓦楞纸板生产线：

| 1 | Maximum paper width 最大生产纸宽 | 2200mm | 2 | Design production speed设计生产速度 | 150m/min |
| --- | --- | --- | --- | --- | --- |
| 3 | Three-layer speed 三层工作速度 | 100-120m/min | 4 | Five-layer working speed 五层工作速度 | 80-100m/min |
| 5 | Seven-layer working speed七层工作速度 | ------------------- | 6 | Maximum exchange speed最高换单速度 | 100m/min |
| 7 | Longitudinal cutting paper accuracy 纵切分纸精度 | ±1mm | 8 | Crosscutting precision 横切裁切精度 | ±1mm |
| remarks备注 | The above speed target shall be up to 1800 mm in width, comply with the following paper standards and ensure that the surface temperature of the heated parts of the equipment is 175 ℃. 以上速度指标须达到：生产幅宽1800mm，符合以下用纸标准并保证设备受热件表面温度在175℃之条件。 |
|  | Tissue index 面纸指标 | 100g/㎡--180g/㎡ 环压指数（N.m/g）≥8 (含水分8-10%) |
|  | Core paper index 芯纸指标 | 80g/㎡--160g/㎡ 环压指数（N.m/g）≥5.5 (含水分8-10%) |
|  | Paper index 里纸指标 | 90g/㎡--160g/㎡ 环压指数（N.m/g）≥6 (含水分8-10%) |
| 9 | Corrugated combination楞型组合 | A\C\B\E |
| 10 | Steam requirement 蒸汽要求 | Maximum pressure 最高压力16kg/cm2 | Common pressure 常用压力10-12kg/cm2 | Dosage 用量4000kg/Hr |
| 11 | Power demand 电力需求 | AC380V 50Hz 3PH | Installed capacity 装机容量≈220KW | Common power 常用功率≈150KW |
| 12 | compressed air 压缩空气 | Maximum pressure 最高压力9kg/cm2 | Common pressure 常用压力4-8kg/cm2 | Dosage 用量1m3/min |
| 13 | space usage 占用空间 | ≈Lmin70m*Wmin10m*Hmin5m(as Party B provides audited drawings) 实际以乙方提供经审核图纸为准 |

※Configuration instructions for single machine

单机配置说明

1、ZJ-V5B hydraulic shaftless mill roll stand 全液压无轴纸架

ⅰ、Structural features结构特点：

★Adopt hydraulic drive to complete the paper clamping, loosen, remove for the medium, translation left and right and others，the lifting of the paper adopts hydraulic drive.

采用全液压驱动来完成原纸夹紧、松开、移动对中、左右平移等动作，原纸升降采用液压驱动。

★Brake adjustable adopts multipoint braking system.

刹车调整采用多点式刹车系统。

★Each paper rack is equipped with two paper carts that can be served simultaneously from both sides.  每台纸架配两台上纸小车从两侧可同时上纸。

ⅱ、Technical parameter技术参数：

- Paper clip range  maximum : 2200mm     minimum : 1000mm

夹纸范围：最大： 1800mm    最小：1000mm

- Folder diameter  maximum : 1500mm     minimum : 350mm

夹纸直径：最大：￠1500mm    最小：￠350mm

3、Main shaft diameter of paper holder：￠240mm   纸架主轴直径：￠240mm

4、Gas source work pressure（Mpa）：0.4---0.8Mpa 气源工作压力（Mpa）：0.4---0.8Mpa

ⅲ、 Hydraulic system parameters  液压系统参数：

- Work pressure（Mpa）:16---18Mpa                工作压力（Mpa）:16---18Mpa

- Lifting hydraulic cylinder：￠100×440mm          升降液压缸：￠100×440mm

- Clamping hydraulic cylinder：￠63×1300m          夹紧液压缸：￠63×1300mm

- Hydraulic station motor power：3KW --380V -- 50Hz   液压站电机功率：3KW --380V -- 50Hz

- Solenoid valve voltage：220V  50 Hz               电磁阀电压：220V  50 Hz

2、paper trolley、track上纸小车、导轨

ⅰ、Structural features结构特点：

★Push the roller in place将卷筒纸推送到位。

★Track whole buried, The main frame of the 14th channel with ¢ 20mm cold drawn  round  welding，the track length 6000mm。

轨道整体埋地，主架为14号槽钢与￠20mm冷拔圆钢焊接，地轨长度6000mm。

★Each paper with two stage paper trolley,and the paper from the two sides at the same time。每台纸架配两台上纸小车从两侧可同时上纸。

4、RG-1-600 top（core）paper preheater   RG-3-600 three preheater

R06B面（芯）纸预热器 、RG-3-600三重预热器

ⅰ、Structural features结构特点：

★The preheating roller is designed with butterfly head, which conforms to the first class national standard of pressure vessel and has the certificate of pressure vessel.

预热辊采用蝶型封头设计，符合一类压力容器国家标准，并附有压力容器证书。

★The roll surface after precision grinding, fine grinding and hard chromium plating processing，surface friction is small and durable。

各辊表面经精密磨削后精磨并镀硬铬处理，表面摩擦力小，耐用。

★Electric adjustment wrap angle , wrap angle can be rotated within 360 °to adjust the paper heat area . 电动调整包角，包角可在360°范围内旋转调节纸张受热面积。

ⅱ、Technical parameter技术参数：

★Effective width：2200mm                       工作幅宽：2200mm

★Diameter of the preheat roller：￠600mm         预热辊直径：￠600mm

★Diameter of the angle：￠110mm×2             包角轴直径：￠110mm×2

★Steam temperature：150-200 ℃                蒸汽温度：150-200℃

★Steam pressure：0.8-1.3Mpa                   蒸汽压力：0.8-1.3Mpa

★Motor power：250W  short（S2）work system   电机功率：250W    短时（S2）工作制

4、SF-320C fingerless type single facer  SF-320C吸附式单面机

ⅰ、Structural features结构特点：

★Adopt hood suction structure，matched high pressure powerful fan. Gas supply and electrical control cabinet to focus on the same operation, the operating side full cover closed.

采用罩吸式结构，配高压强力风机。气源及电气控制集中于同一操作柜，操作侧全封闭全罩。

★High quality resin sand casting，wall thickness 200mm。Adopt independent gear box, Universal joint transmission structure.

优质树脂砂铸件，墙板厚度200mm。采用独立变速箱，万向节传动结构。

★install the lifting trolley on the conveyor bridge,Need to use the car will tile roll assembly and pressure roller, such as convenient and quick.

在输送天桥上面加装了吊装小车，需要时利用该车将瓦辊总成及压力辊等取出，方便快捷。

★Glue roller unit structure with the overall relocation，Maintenance can sway the machine at the overall maintenance，improve the working efficiency。

涂胶辊单元采用整体外移式结构，维护时可整体侧移出机处进行维护，提高了工作效率。

★The humidity control apparatus equipped with a spray, so flute type to maintain good stability of deformation, avoid dry。

配用喷雾调湿装置，使瓦楞楞型保持良好的变形稳定性，避免干裂。

★Automatic circulation system for glue, two-cylinder pneumatic gluing device, with good cushioning effect.

采用自动循环式供胶系统，双气缸气动上胶装置，具有良好的缓冲效果。

★Glue department using integrated slide structure，Glue roller surface after grinding engraved with 32 lines and pit-style textured hard chrome plating.

涂胶部采用整体式滑板结构，涂胶辊表面经精磨后刻有32线凹坑式网纹并镀硬铬处理。

★Corrugated roller adopt tungsten carbide dealing，diameter of the main corrugated roller¢ 320mm，Quenched→rough car→bore fine boring→shaft head shrunk-on→welding → tempering to stress→fine cars→coarse grinding→IF quenching→CNC grinding machine grinding→tungsten carbide dealing，hardness of surface is HV58degrees。

瓦楞辊材质48CrMo合金钢，瓦楞主辊直径¢ 320mm，经调质→粗车→内孔精镗→轴头烘装→焊接 → 回火去应力→精车→粗磨→中频淬火→数控磨床精磨→碳化钨处理。

★Active force variable frequency motor drive, energy efficient, low failure rate。

主动力采用变频电机驱动，节能高效，故障率低。

★Glue wide electric adjust to changes in the width of the paper used。

涂胶宽幅电动调整，以适应所用原纸宽度变化。

★Amount of glue size with electric adjustment, touch screen display and operation of the encoder transmission coating gap, high accuracy。

涂胶量大小采用电动调整，触摸屏显示及操作，通过编码器传输涂胶间隙，精确度高。

★Power and operating parts with a safety net to ensure the safety of personnel in the operation of machinery。

动力及操作部位配有安全防护网，以确保人员在机器运转时的安全。

ⅱ、Technical parameter技术参数：

★Effective width：2200mm                工作幅宽：2200mm

★Operation direction：left or right（determined in accordance with customer plant）

操作方向：左置或右置（根据客户厂房确定）

★Design speed：150m/min                设计速度：150m/min

★Temperature range：160—180℃         温度范围：160—180℃

★Corrugated flute:（UV type or UVV type） 瓦楞楞型（UV型或UVV型）：

ⅲ、Roller diameter parameter辊类直径参数：

★Corrugated roll diameter瓦楞辊直径： up￠313mm      down￠316mm

★Pressure roll diameter压力辊直径： ￠320mm

★Glue roller diameter涂胶辊直径： ￠240mm

★ Fixed paste roller定糊辊： ￠140mm

★Preheater diameter预热器直径： ￠402mm

ⅳ、Powered motor parameters动力电机参数：

★Main frequency drive motor：18.5KW     主变频驱动电机：18.5KW

★Suction motor：11KW                   吸风电机:11KW

★Glue reducer：100W                    调胶减速机：100W

★Glue adjusting  motor：200W*2          隔胶调整电机：200W *2

★Glue pump motor：2.2KW               胶泵电机：2.2KW

5、ZDF conveyor bridge  输送过桥

ⅰ、Structural features结构特点：

★This part is the main beam of the 20th channel, 16-beam, angle iron 63, column, etc. are connected.

本部分是主梁为20号槽钢、16号工字钢、63号角钢、立柱等连接而成。

★Both sides of the security fence, ladder , high-strength save people the word pedals, ensure the safety of personnel and easy to operate.

两侧均有安全护栏、梯子（用8号小槽钢制作）、高强度人字踏板，确保人员的工作安全以及操作方便。

★Pull the paper shaft surface tension axis, feeding shaft by grinding hard chrome plated.

牵纸轴、张紧轴、输纸轴等表面经磨削加工镀硬铬处理。

★Vacuum tension control, 5-inch suction tube, plus regulating valves, air flow can be infinitely adjustable.

真空吸附张力控制，吸风管5寸，加调节阀门，风量可无级可调。

★Dual front bezel correction guide column positioning, screw driver, fast and accurate positioning, walking steadily.

纠偏挡板前采用双导向柱定位，丝杠驱动，定位快速准确，行走平稳。

ⅱ、Roller diameter parameter辊类直径参数：

★Paper roll and a tension roller diameter:￠130mm         上纸辊及张紧辊直径：￠130mm

★Conveying roller diameter：￠180mm                    输送辊直径：￠180mm

★Active tension roller diameter：￠85mm                  主动张紧辊直径：￠85mm

★Diameter of over paper rollers and guide rollers：￠110mm 过纸辊及导纸辊直径：￠110mm

★Paper towing shaft diameter：￠110mm                  上纸拖带轴直径：￠110mm

ⅲ、Powered motor parameters动力电机参数

★Corrugated single paper lift motor：2.2KW                单面瓦楞纸提升电机：2.2KW

★The bridge adsorption motor：2.2KW                     过桥吸附风机：2.2KW

★Wide motor tune cardboard：250W                      调纸板宽幅电机：250W

6、GM-20  Double glue machine二层涂胶机

ⅰ、Structural features结构特点：

★After the surface of cots is adjusted and tempered, the inner hole is processed, the dynamic balance surface is polished and there are 32 lines of concave net pattern, the glue is uniform and the amount of glue consumption is less.

涂胶辊表面经调质后，内孔加工，做动平衡表面精磨并刻有32线凹坑式网纹，涂胶均匀，耗胶量少。

★The rotation of the cots is controlled by the variable frequency motor and frequency conversion, and the frequency control ensures that the linear speed of the cots is synchronized with the two sides, and it can operate independently.

涂胶辊的转动由变频电机加变频控制，由变频控制保证涂胶辊的线速度与双面机同步，又可以独立运转。

★Coating electric adjustment glue amount of digital display. Automatic circulation of glue, can effectively control the amount of glue, avoid glue precipitation, ensure good glue and save glue.涂胶电动调整胶量数显。自动循环供胶，能有效控制胶量，避免胶水沉淀，保证良好的胶水和节约胶水。

★All roller surfaces are ground after hard chromium plating.

所有辊轴表面均经过磨削处理后镀硬铬。

★ The speed signal of double-sided machine is measured to realize synchronous operation with it. The rubber coating machine is displayed with man-machine interface, which can be used for data setting and easy to operate.

测取双面机速度信号，以实现与其同步运转。涂胶机采用人机界面显示，可进行相关数据设定，操作简便快捷。

★Electrical design, construction production process, follow the national standards, low failure rate, easy maintenance。

电器设计、生产施工工艺，遵循国家标准规范，故障率低，维护简单。

ⅱ、Technical parameter技术参数：

★Effective width：2200mm                         工作幅宽：2200mm

★Operation direction：left or right（determined in accordance with customer plant）

操作方向：左置或右置（根据客户厂房确定）

★Design speed：150m/min                        设计速度：150m/min

★Gas supply system：0.4—0.6Mpa                 气源系统：0.4—0.6Mpa

★Preheat cylinder temperature range：150—200℃   预热缸温度范围：150—200℃

★Steam pressure:0.8—1.2Mpa                     蒸汽压力：1.12—1.3Mpa

ⅲ、Roller diameter parameter辊类直径参数：

★Glue roller diameter：￠269mm                   涂胶辊直径：￠269mm

★Doctor roller diameter：￠142mm                 定糊辊直径：￠142mm

★Over the paper roll diameter：￠110mm            过纸辊直径：￠110mm

ⅳ、Powered motor parameters动力电机参数：

★Glue roller initiative frequency motor：3KW         涂胶辊主动电机：    3KW

★Sizing Reducer:：250W                          胶量调整减速机：    250W

★Pressure roller clearance adjustment motor： 250W 压力辊间隙调整电机：  250W

★Glue pump motor：2.2KW                        胶泵电机：2.2KW

- SM-F type double facer双面机

ⅰ、Structural features结构特点：

★The surface of the heating plate is grinded, the width of the hot plate is 600mm, there are 12 heating plates, the cooling setting is 4 meters.The heating plate is made of vessel plate, which conforms to the national first-class pressure vessel standard, with pressure vessel certificate and inspection certificate.

加热板表面经研磨处理，热板宽度600mm，共12块加热板，冷却定型部长4米。加热板采用容器板制作，符合国家一类压力容器标准，附有压力容器证书及检验合格证。

★The upper conveyer belt rectifies the right and left side to adopt the pneumatic automatic correction deviation.

上输送带左右纠偏调整采用气动自动纠偏。

★Heating plate heat transfer pipe temperature control sub-four-segment, with a temperature display.  加热板的导热配管分四段控制温度，设有温度显示。

★Double cylinder S type cotton belt tensioning device is used for upper cotton belt.

上棉织带采用双气缸S型棉织带张紧装置。

★The lower belt adopts pneumatic tension, pneumatic correction.下带采用气动张紧，气动纠偏。

★Drive roller coated with attached wear-resistant rubber ，showed a herringbone structure，With a high, ensure smooth cardboard output。

驱动辊表面包附耐磨像胶，呈人字型结构，并带有中高，保证纸板平整输出。

★Main drive motor for frequency conversion motor，low-speed torque，wide speed range ,reliable, and easy maintenance.

主驱动电机为变频调速电机，低速力矩大，调速范围广，使用可靠，维护简单。

★Hot plate internal for partition isolation structure,s-shaped flow of steam，Steam, water separation function significantly improves the utilization of steam。

热板内部为隔板隔离结构，使蒸汽呈S形流向，汽、水分离功能明显，提高了蒸汽利用率。

ⅱ、Technical parameter技术参数：

★Temperature requirement：160—200℃                  温度要求：160—200℃

★Steam pressure：0.8-1.3MPa                           蒸汽压力：0.8-1.3MPa

★Air source pressure：0.6—0.9MPa                      气源压力：0.6—0.9MPa

★Cooling stereotypes length：4m                         冷却定型长度：4米

★Heating plate quantity：16 pieces                       加热板数量：16块

ⅲ、Roller diameter parameter辊类直径参数：

★Upper drive rubber roller diameter：￠700mm            上驱动胶辊直径：￠700mm

★Lower drive rubber roller diameter ：￠400mm           下驱动胶辊直径：￠400mm

★Former follower with roller diameter：￠215mm           前从动带辊直径：￠215mm

★Back setting belt driven roller diameter：￠215mm        后定型从动带辊直径：￠215mm

★Platen roller：￠70mm                                 压带辊直径：￠70mm

★Setting roller diameter：￠86mm                        定型托辊直径：￠86mm

★Upper belt tension roller diameter：￠155mm             上带张紧辊直径：￠155mm

★Upper roll diameter with detuning：￠130mm             上带调偏辊直径：￠130mm

★Entrusted with the roll diameter lower belt：￠130mm      下带托带辊直径：￠130mm

★Lower belt tension roll diameter: ￠130mm                下带张紧辊直径：￠130mm

Note: All the roller surface after grinding are hard chrome plated。

注：所有辊轴表面均为磨削后镀硬铬处理。

ⅳ、Powered motor parameters动力电机参数：

★Main drive motor power：30Kw                          主驱动电机功率：30KW

8、ZQS Thin knife slitting薄刀纵切压痕机

ⅰ、Structural features结构特点：

★Overcome the conventional type of pole, cutting pressure lines appear when collapsed cardboard cut phenomenon, cutting board smooth, quality has improved significantly。

克服了常规的双刀型、分切压线机在裁切时出现压塌纸板的现象，切板光滑，质量明显提高。

★The whole machine can remove left and right,cycloid reducer to adjust。

整机可以左右移动，以摆线式减速机调节。

★Cutter and easy to adjust the pressure line, the error ± 0.5mm, automatic sharpening device, you can achieve timing Brothers, with intermittent Brothers and other features.

切刀和压线调整方便，误差±0.5mm，有自动磨刀装置，可以实现定时磨刀，与间隔性磨刀等多种功能。

★The machine adopt five knives eight lines,the blade is made of tungsten alloy steel, the using life is not less than 3 million running meters。

本机采用5刀8压线式，刀片用钨合金钢制作，使用寿命不小于300万跑米。

ⅱ、Technical parameter技术参数：

★Effective width：2200mm                         工作幅宽：2200mm

★Design speed: 120 m / min                        设计速度：120m/min

★Mechanical configuration: 5 knives and 8 lines       机械配置： 5刀8线

★Minimum cutting width: 135mm                    最小切纸宽度：135mm

ⅲ、Powered motor parameters动力电机参数：

★Line cutter line motor:0.4KW                       排刀线电机:0.4KW

★Knife wheel drive motor:5.5KW                    刀轮驱动电机:5.5KW

9、NC-150  NC cutter helical knives  电脑螺旋刀横切机

ⅰ、Structural features结构特点：

★It can store 200 units orders，replace the cutter specifications quickly and accurately，changing orders without stop,And enables networked computers to facilitate production management.

可储存200组定单，更换切纸规格迅速准确，不停机换单，并可实现计算机联网，方便生产管理。

★Knife shaft drive gears are precision forged steel induction hardening, backlash-free transmission, advanced keyless connection, high transmission accuracy。

刀轴传动齿轮采用精锻钢材料高频淬火，实现无侧隙传动，采用先进的无键连接方式，传动精度高。

★Cutting machine adopts inlaid front steel blade knife spiral structure, serrated knife. scissors, shears, shear force, long blade life。

横切机刀片采用镶锋钢螺旋刀结构，锯齿刀型。剪刀式剪切，剪切力小，刀片寿命长。

★Around feed rollers are used  the sun gear platen way, smooth delivery, pressure evenly, easy to crush plate board or cause blockage。

前后送纸轮均采用太阳轮压纸方式，输送平稳，压力均匀，不易压坏板板或造成堵塞。

★This type of brake is energy storage type (non-energy brake), so in the process of production, the average power consumption is 1 / 3 of that of the ordinary NC cutting machine, saving more than 70% of electricity and achieving the goal of saving money.

本机型是储能式制动（非能耗制动），故在生产过程中低能耗，平均用电量是普通NC切断机的1/3，节省电70%以上，达到省钱的目标。

★Exact and adjustable no gap gear to ensure precise blade engagement, running balance.

精密可调无隙齿轮，确保刀口精确啮合，运行平衡。

★Independent oil pump and filter are used to distribute two sets of copper pipes in each gear position to feed oil, lubricate and cool.

采用独立油泵和过滤器配合两组紫铜管分布于各齿轮位供油，润滑和冷却。

★Knife roller: fine quality forged steel material, the balanced, with good stability.

刀辊：优质精锻钢材质，经平衡处理，具有良好的平稳性。

ⅱ、Technical parameter技术参数：

★Effective width：2200mm                          工作幅宽：2200mm

★Operation direction：left or right（determined in accordance with customer plant）

操作方向：左置或右置（根据客户厂房确定）

★Design speed: 150 m / min                         设计速度：150m/min

★Mechanical configuration: computer helical cutter crosscutting  机械配置：电脑螺旋刀横切

★Minimum cutting length：500mm                    最小切纸长度：500mm

★Maximum cutting length：9999mm                  最大切纸长度：9999mm

★Cutter accuracy: Uniform for ± 1mm,  non-uniform to ± 2mm

切纸精度：匀速为±1mm，非匀速为±2mm

★Equipment size: Lmx4.2 Wmx1.2 Hmx1.4            设备尺寸：Lmx4.2*Wmx1.2*Hmx1.4

★Single machine weight: maximum 3500kg            单机重量：最大3500Kg

ⅲ、Roller diameter parameter辊类直径参数：

★Cross on the knife shaft center distance：￠216mm    横切上、下刀轴中心距：￠216mm

★Before the lower conveying roller diameter  ￠156mm  前下输送辊直径  ￠156mm

★After the lower conveying roller diameter：￠156mm   后下输送辊直径：      ￠156mm

★Roll diameter: 160mm。                            牵纸辊直径：￠160mm

★Output solar wheel diameter: 160mm                 输出太阳轮直径： ￠160mm

Note: all roller shafts after grinding, the surface of hard chromium plating (except upper, lower tool shaft).

注：所有辊轴均经磨削后，表面镀硬铬处（上、下刀轴除外）理。

ⅳ、Powered motor parameters动力电机参数：

★main drive motor power：22Kw   Full AC synchronous servo

主驱动电机功率：22KW             全交流同步伺服

★Before feeding motor power：3Kw（Frequency Control）

前后输纸电机功率：3KW（变频调速）

10、DM-XLM Automatic small gantry stacking machine

全自动龙门式堆码机

ⅰ、Structural features结构特点：

★Gantry stacking。Changing single time is 5seconds，automatic counting, automatic cross out automatically for a single.

龙门式堆码。换单时间5秒，可自动计数，自动横出，自动换单。

★Synchronized with the production management system，order mangement，Centralized management，do not slow down automatically for a single.

与生管系统同步，订单管理，集中管理，不降速自动换单。

★The waste of changing single tube was less than 700 mm.生管换单浪费小于700mm。

★crawler stacking platform，AC servo control movements，Stacking smooth, neat;履带式堆码平台，交流伺服控制升降，堆码平稳、整齐；

★When stacking reaches a set number of automatic frequency control smooth laterally out of paper；

堆码达到设定数量时变频控制自动平稳横向出纸；

★Tailgate AC servo control positioning for a single automatic, rapid, precise adjustment；

后挡板交流伺服控制定位，换单时自动、快速、精确调整；

★Tailgate automatically shift for small orders stacking；

后挡板可自动移位，适合小订单堆码；

★Delivery side of the standard electric transport planes, and duplex trolley。

输送侧标配电动输送架，及双工位台车。

★Independent sealed control cabinets, electrical equipment operating under clean environment；

独立密封控制柜，电气设备在无尘、环境下运行；

★Color touch-screen display for easy on-site operation。

彩色触摸屏显示，方便现场操作。

★Fully automatic operation control, improve efficiency and save manpower, reduce labor intensity；全自动运行控制，提高效率，节省人力，降低操作人员劳动强度；

ⅱ、Technical parameter技术参数：

1、Effective width：2200mm                  最大工作宽幅：2200mm

2、Operation direction：left or right（determined in accordance with customer plant）

操作方向：左置或右置（根据客户厂房确定）

- Working speed: 150m / min                工作速度：150m/min

4、Maximum stacking height: 250mm          最大堆积高度：250mm

5、Maximum stacking length: 3500mm         最大堆积长度：3500 mm

6、Shape size: 13m*2.5m*2.2m               外形尺寸：13m*2.5m*2.2m

11、ZJZ glue station system   制胶站系统

ⅰ、Structural features结构特点：

★Provide the starch adhesive to the corrugated single facer , glue machine and some other gluing equipment.

为单面瓦楞机，涂胶机等用胶设备提供淀粉粘合剂。

★Horizontal glue machine can meanwhile matched  with main body glue and carrier glue, and mixing, glue large。

卧式制胶机可同时配制主体胶和载体胶，并混合搅拌，制胶量大。

★Making room storage barrels adhesive solution was to use the glue pump rubber equipment storage barrels, adhesive solution for equipment。

制胶房储存桶胶液被胶泵输送到各个用胶设备的储存桶里，为设备提供胶液。

★Storage barrels, plastic barrels with mixing device, avoid glue solution precipitation agglomerate。

储存桶、供胶桶自带搅拌装置，避免胶液沉淀结块。

★System unit with carrier vessel, main tank, storage tank, and send the glue pump, the back glue

pump, etc。制胶装置分别有载体罐，主体罐，贮存罐，及送胶泵、回胶泵等组成。

★Glue system adopt glue cycle,rest glue go back to the glue square cylinder,Liquid level float automatic control,the back glue a bucket of glue liquid being beaten back with glue equipment storage bucket，cycle for glue，Save the glue solution，prevent the glue solution in the rubber plate pasting and caking precipitation.

制胶系统采用循环供胶，余胶流到回胶方桶里，液位浮球自动控制，回胶方桶里的胶液被打回到用胶设备的储存桶里，进行循环供胶，节约胶液，防止胶液在胶盘中糊化和结块沉淀。

★Work has been completed, the residual gum dividend total pipeline with rubber equipment rubber pumped back rubber room storage barrels, for next time use。

工作完毕后，各用胶设备余胶被除数总管道胶泵抽回胶房储存桶里，供下次使用。

★Responsible for technical guidance, teaching adhesive dispensing process。

负责技术指导，传授粘合剂配制工艺。

ⅱ、Technical parameter技术参数：

★Horizontal body glue mixer：one                   卧式主体胶搅拌机： 1台

★Carrier glue mixer：one                           载体胶搅拌机：1台

★Storage glue mixer：one                          储存胶搅拌机：1台

★Plastic buckets on coater：one                    涂胶机上胶桶：1件

★Coating machine back plastic buckets :one        涂胶机回胶桶：1件

★Plastic buckets on single machine :two              单面机上胶桶：2件

★Single machine back plastic buckets：two           单面机回胶桶：2件

★Lose glue dispensing pumps：four                  输胶胶泵：4台

ⅲ、Glue barrel diameter parameters胶筒直径参数：

★Horizontal body glue mixer：1250mm×1000mm×900mm

卧式主体胶搅拌机：1250mm×1000mm×900mm

★Carrier glue mixer  diameter：  ￠800mm×900mm

载体胶搅拌机直径：￠800mm×900mm

★Diameter plastic bucket on Glue：￠800mm×1000mm

涂胶上胶桶直径：￠800mm×1000mm

★Plastic buckets on single machine：￠800mm×1000mm

单面机上胶桶：￠800mm×1000mm

★Storage tank diameter：￠1200mm×1200mm

储存胶桶直径：￠1200mm×1200mm

ⅳ、Powered motor parameters动力电机参数：

★Horizontal body glue mixer：3Kw                          卧式主体胶搅拌机：3KW

★Carrier glue mixer：2.2Kw(Ordinary three-phase)            载体胶搅拌机：2.2KW(普通三相)

★Output plastic pump motor ：2.2Kw（Ordinary three-phase） 输胶泵电机：2.2KW（普通三相）

★Storage Tank Motor：1.5Kw（Ordinary three-phase）        储存胶桶电机：1.5KW（普通三相）

12、ZQ steam system蒸汽系统

ⅰ、Structural features结构特点：

★Production line for hot heating energy delivery device to maintain a stable operating temperature。为生产线各用热设备输送加热能源，保持工作温度的稳定。

★All units are designed to be independent small unit for the steam system, segmented temperature control, energy saving, easy to adjust。

各机组均设计成独立小单元供汽系统，分段控温，节约能源，调整方便。

★By adjusting the steam pressure monitor dial to exercise control over the operating temperature, and a pressure。

通过调节蒸汽压力实行对工作温度的控制，并设有压力监视表盘。

★Each group has a hydrophobic unit emptying bypass, when rapid shutdown cooling equipment。每组疏水单元均设有排空旁通，停产时设备降温迅速。

★Float trap 1/2 metal hose and connect the bypass valve, plug valve injection。

倒桶疏水器，不锈钢止回阀，不锈钢芯截止阀门。

★Between the piping system and the rotary heating member in order to achieve a flexible metal hose connection, to extend the service life of the rotary joint。

管道系统与旋转加热部件间以金属软管实现柔性连接，以延长旋转接头的使用寿命。

★All steam pipes are made of seamless steel tubes, to ensure safety for use under normal pressure。

所有机内蒸汽管道均选用无缝钢管，确保正常压力作用下使用的安全性。

ⅱ、Technical parameter技术参数：

★Steam consumption: about 2.5-3T/h          蒸汽耗量：约2.5-3T/h

★Equipped with boiler：4t/h                   配用热源：4t/h

★Equipped with boiler pressure：1.25MPa   Pipe temperature：170—200℃

蒸汽压力：1.25Mpa       管道内温度：170—200℃

※Main parts, raw materials, origin (brand)

主要部件、原材料、产地（品牌）

| Name of main parts 主要件名称 | Brands or place of origin 品牌或产地 | Material 材质 |
| --- | --- | --- |
| Main motor 主电机 | Hebei hengshui 河北衡水 |  |
| Reducer 减速机 | Shandong, De zhou,Jin zhan 山东德州金展 |  |
| Bearing 轴承 | HRB、ZWZ、CYC 哈、瓦、洛 |  |
| Seat belt bearing 带座轴承 | Zhengjiang five rings 浙江五环 |  |
| Contactor, relay 接触器、继电器 | France Schneider 法国施耐德 |  |
| Paper clip head 夹纸头 | Xusheng 旭升 | 3 inches and 4 inches in common 3英寸、4英寸共用 |
| Steam rotary joint 蒸汽旋转接头 | Shandong Quanzhou Yujie 山东泉州玉杰 |  |
| Preheating 预热缸 | Hangang or Jigang 邯钢或济钢 | Q235Bpressure vesselplate Q235B压力容器板 |
| Trap 疏水阀 | Beijing 北京 | Floating ball type 浮球式 |
| Wallboards and bases 墙板及底座 | Self birth 自产 | HT200 |
| Air cylinder 气缸 | Zhejiang Sanzheng 浙江三正 |  |
| Heating appliance 加热板 | Tiangang or Jigang 天钢或济钢 | Fabrication of Q235B Container Plate Q235B容器板制作 |
| Cotton tape 棉织带 | Shenyang 沈阳 | Thickness 10mm 厚度 10mm |
| hydraulic pressure station 液压站 | Hebei 河北 |  |
| photoelectric switch 光电开关 | South Korea Autonics 韩国Autonics（奥托尼克斯） |  |
| electromagnetic valve 电磁阀 | Adriatic 亚德客 |  |
| Belt 同步带 | Germany OPTIBELT 德国奥比 |  |
| Tensioning sleeve 涨紧套 | Xianyang chaoyue 咸阳超越 |  |
| proximity switch 接近开关 | OMRON, Japan 日本欧姆龙OMRON |  |
| Flying shear servo control system飞剪伺服控制系统 | Germany Kobe 德国科比 |  |
| Motion control board 运动控制板 | Germany 德国MKS-CT150 |  |
| Touch screen 触摸屏 | Kunlun tongtai 昆仑通态 |  |
| Sun wheel 太阳轮 | Shenzhen China 中国深圳产 |  |
| Inverter、PLC 变频器、PLC | Taiwan Delta 台湾台达 |  |
| pneumatic component 气动元件 | Adriatic 台湾亚德客 |  |