WJ150-1800 -I type three layer corrugated board production line

WJ150-1800-Ⅰ型三层瓦楞纸板生产线

Equipment configuration and technical specification

设备配置及技术说明

已通过ISO：9001-2008标准质量管理体系认证

创新包装科技，打造一流品牌

Hebei Dongguang Hengchuangli Carton Machinery Co., Ltd  Company

highway cangzhou county, hebei province

| Production line configuration list 生产线配置清单 |
| --- |
| Models规格型号 | Name 设备名称 | QTY 数量 | Unit price 单价 （万元） | Remark 备注 |
| ZJ-V5B | Hydraulic shaftless mill roll stand 全液压无轴 纸架 | 3台 （set） |  | Spindle ¢ 240mm, hyperbolic heavy rocker, expand chuck , multi-point brake, hydraulic drive lifting, panning left and right on the middle. 主轴￠240mm，双曲线重型摇臂，齿式夹纸头，多点式刹车,液压驱动升降，左右平移，对中等。 导轨长度6000mm，采用中板焊接。 |
|  | Rail and Tracks 上纸小车 | 6台 （set） |  | The guide track is 6000mm and the trolley is welded with 10mm。 导轨长度6000mm，小车采用10mm中板焊接。 |
| R09B | Pre-heater 面纸预热器 | 1台 （set） |  | Roller ￠900 mm, Pressure vessel certificate Electric adjustment package Angle.Angle can be adjusted within the range of 360 ° paper heated area. 辊筒￠900mm，含压力容器证书。电动调整包角。包角可在360°范围内调节纸张受热面积。 |
| R09B | Pre-heater 芯纸预热器 | 1台 （set） |  | Roller ￠900 mm, Pressure vessel certificate Electric adjustment package Angle.Angle can be adjusted within the range of 360 ° paper heated area. 辊筒￠900mm，含压力容器证书。电动调整包角。包角可在360°范围内调节纸张受热面积。 |
| SF-320c | Fingerless type single facer 单面瓦楞机 | 2台 （set） |  | Corrugated main roller ￠320mm，material with 48CrMo alloy steel,tungsten carbide dealing,Tile roll modular group lifting transfer.Airbag ballasting structure，import main bearing，PLC automatic control glue，HMI touch screen，Breaks automatic parking relief，steam heating way.瓦楞主辊￠320mm，材质采用48CrMo合金钢。碳化钨处理，瓦辊模块式成组吊换。气囊压载结构，进口主轴承，PLC自动控胶，人机界面触摸屏，断纸自动停车卸压，蒸气加热方式。 |
| RG-2-900 | Double Pre-heater 二重预热器 | 1台 （set） |  | Roller ￠900 mm, Pressure vessel certificate Electric adjustment package Angle.Angle can be adjusted within the range of 360 ° paper heated area. 辊筒￠900mm，含压力容器证书。电动调整包角。包角可在360°范围内调节纸张受热面积。 |
| GM-20 | glue machine 涂胶机 | 1台 （set） |  | The diameter of the roller is 269mm. Independent variable frequency motor drive, manual。 Adjustment of glue clearance. 涂胶辊直径269mm。独立变频电机驱动，手动调整涂胶间隙。 |
| ZDF | Conveyor bridge 输送过桥 | 1套 （set） |  | Adopt independent variable frequency motor drive, pull paper adsorption tensioning device. 采用独立变频电机驱动，牵纸吸附式张紧装置。 |
| SM-10 | Double facer 双面机 | 1套 （set） |  | Drying department is 600mm*12 heating plate, pneumatic lifting roller, adopting the compact pressure roller. 烘干部600mm*12块加热板，气动升降压辊,采用密集型压辊。 |
| Type | Thinknife cuttingindentation machine - all electric type 薄刀纵切压痕机-全电动型 | 1台 （set） |  | Product overview:Eight roll type slitter scorer machine,adopt two shafts in front and back of the slitter,can minimize the length of paperboard machining.Not only meet the conventional cutting board size,can also be used for cutting small cardboard pallets and other specifications.Electric adjusted the space of slitter blade,auto locking,improve the efficiency. 加轴型薄刀纵切压痕机，由于采用前后双胶计 ，大大减少对纸板长度要求，不但满足常规纸板的分切尺寸，还可以用于分切垫板等小规格纸板。电动调整分切刀和压线轮工作距离，自动锁紧，提高工作效率。 |
| NC-120 | NC cutter helical knives电脑螺旋刀横切机 | 1台 （set） |  | Ac servo control, energy storage brake, helical knife type structure, oil-immersed gear drive, 10.4-inch touch screen display. 全交流伺服控制，储能式制动，螺旋刀式结构，油浸式齿轮传动，10.4寸触摸屏显示。 |
| DMT- 120 | Carton stacker直角堆码机 | 1台 （set） |  | Electric adjusting board dimensions, pneumatic control horizontal output board.Take the count 电动调整纸板尺寸，气动控制横向输出纸板。带计数. |
| ZJZ | Glue station system 制胶站系统 | 1套 （set） |  | The pipeline customer is prepared.The glue device is composed of carrier tank, main tank, storage tank, and glue pump and return pump. 管道客户自备。制胶装置分别有载体罐、主体罐、贮存罐、及送胶泵、回胶泵组成。 |
| QU | Air supply system 气源系统 | 1台 （set） |  | Customer's own gas source. 客户自备气源。 |
| ZQ | Steam system蒸汽系统 | 1套 （set） |  | Contain the valve of pipeline, steam trap,instrument and other steam components. 含设备内管道阀门、疏水阀、仪表等蒸汽元件，客户自备热源及管道。 |
| 合计 | Ex-factory price of RMB：（ price include tax） ￥： 人民币： ￥： |
| Self-contained part 客户自备部分 1、Steam heating system：proposal with 4000Kg/Hr of a steam boiler pressure:1.25MPa steam pipeline。蒸汽供热系统：建议配4000Kg/Hr蒸汽锅炉一套， 压力为1.25Mpa，蒸汽管道。 2、Air compressed machine、air pipeline、glue conveying pipe。 空气压缩机、空气管道、胶液输送管道。 3、Power supply、wires connected to the operation panel and line pipe。 电源、电线接至操作柜及线路管道。 4、Water sources、water pipelines、buckets and so on。水源、输水管道、水桶等。 5、Water, electricity, gas flush mounting civil foundation。水、电、气地基平面安装土建工程。 6、Test with the base paper、corn starch (potato)、Industrial use caustic soda、borax and other material。试车用原纸、玉米（薯类）淀粉、工业用烧碱、硼砂等材料。 7、Oil equipment、lubricating oil、hydraulic oil、lubricating grease。 设备用机油、润滑油、液压油、润滑脂。 8、Installation、commissioning of food, accommodation。And provide installers with the installation.安装、调试人员的饮食、住宿。并提供安装工人配合安装。 |

※Main technical parameter and requirements

生产线主要技术参数及要求

Model: WJ150-1800 - I type three layer corrugated board production line:

型号：WJ150-1800-I 型三层瓦楞纸板生产线

- Maximum production width of corrugated board：1800mm

瓦楞纸板最大生产宽度 ：1800mm

- Design speed150m/min             设计速度：150m/min

- Economic speed 100-120m/min      经济速度：100-120m/min

Note: line speed test paper should meet the following requirements: (equipment surface temperature is not lower than 172 ℃ or above)

注：生产线速度试验用纸应符合下列要求：（设备表面温度不低于172℃以上）

*The original paper grade shall not be less than the amount of water in grade B

原纸等级不得低于B级

*The water content of the original paper is about 11% ± 2%

原纸含水量约为：11%±2%

*Surface paper: 100—250g/m2       面纸：100—250g/m2

*core paper:100—250g/m2                  芯纸：100--250g/m2

*Tile paper: 100-200g/m2                     瓦纸：100—200g/m2

4、Corrugated combination: A, C, B, E (or selected by the customer)

瓦楞楞型组合：A 、C、 B、 E（或由客户自选）

5、Steam requirement：             蒸汽所需要求：

*Steam in 1500-2000 kg/Hr        蒸汽量：1500—2000Kg/Hr

*Top pressure: 1.2Mpa             最高压力：1.2Mpa

* pressure: 0.8-1.1Mpa           用压力：0.8-1.1Mpa

6、Power supply：380V     50Hz           Three phase four wire system

电源：380V     50Hz      三相四线制

- The total power about 150KW     The practical power about 80KW(full speed)

设备装机总功率：约150KW            实际用电量：约80KW(全速)

8、Equipment cover an area of about 52m×10m×5m（The specific length is based on the foundation of foundation）

设备占地：约52m×10m×5m(具体长度以地基基础图为准)

- Paper direction: drive left or right set according to the user factory

设备出纸方向：根据用户厂房确定传动左置或右置

10、Equipment applicability, usable A, B, C grade domestic original paper or imported original paper。 设备适用性，可用A、B、C级国产原纸或进口原纸

※Configuration instructions for single machine

单机配置说明

1、ZJ-V5B hydraulic shaftless mill roll stand 全液压无轴纸架

ⅰ、Structural features结构特点：

★Adopt hydraulic drive to complete the paper clamping, loosen, remove for the medium, translation left and right and others，the lifting of the paper adopts hydraulic drive.

采用全液压驱动来完成原纸夹紧、松开、移动对中、左右平移等动作，原纸升降采用液压驱动。

★Brake adjustable adopts multipoint braking system.

刹车调整采用多点式刹车系统。

★Each paper rack is equipped with two paper carts that can be served simultaneously from both sides.  每台纸架配两台上纸小车从两侧可同时上纸。

ⅱ、Technical parameter技术参数：

- Paper clip range  maximum : 1800mm     minimum : 1000mm

夹纸范围：最大： 1800mm    最小：1000mm

- Folder diameter  maximum : 1500mm     minimum : 350mm

夹纸直径：最大：￠1500mm    最小：￠350mm

3、Main shaft diameter of paper holder：￠240mm   纸架主轴直径：￠240mm

4、Gas source work pressure（Mpa）：0.4---0.8Mpa 气源工作压力（Mpa）：0.4---0.8Mpa

ⅲ、 Hydraulic system parameters  液压系统参数：

- Work pressure（Mpa）:16---18Mpa                工作压力（Mpa）:16---18Mpa

- Lifting hydraulic cylinder：￠100×440mm          升降液压缸：￠100×440mm

- Clamping hydraulic cylinder：￠63×1300m          夹紧液压缸：￠63×1300mm

- Hydraulic station motor power：3KW --380V -- 50Hz   液压站电机功率：3KW --380V -- 50Hz

- Solenoid valve voltage：220V  50 Hz               电磁阀电压：220V  50 Hz

2、paper trolley、track上纸小车、导轨

ⅰ、Structural features结构特点：

★Push the roller in place将卷筒纸推送到位。

★Track whole buried, The main frame of the 14th channel with ¢ 20mm cold drawn  round  welding，the track length 6000mm。

轨道整体埋地，主架为14号槽钢与￠20mm冷拔圆钢焊接，地轨长度6000mm。

★Each paper with two stage paper trolley,and the paper from the two sides at the same time。每台纸架配两台上纸小车从两侧可同时上纸。

3、RG-1-900 top（core）paper preheater   RG-2-900 double preheater

R09B面（芯）纸预热器 、RG-2-900二重预热器

ⅰ、Structural features结构特点：

★The preheating roller is designed with butterfly head, which conforms to the first class national standard of pressure vessel and has the certificate of pressure vessel.

预热辊采用蝶型封头设计，符合一类压力容器国家标准，并附有压力容器证书。

★The roll surface after precision grinding, fine grinding and hard chromium plating processing，surface friction is small and durable。

各辊表面经精密磨削后精磨并镀硬铬处理，表面摩擦力小，耐用。

★Electric adjustment wrap angle , wrap angle can be rotated within 360 °to adjust the paper heat area . 电动调整包角，包角可在360°范围内旋转调节纸张受热面积。

ⅱ、Technical parameter技术参数：

★Effective width：1800mm                       工作幅宽：1800mm

★Diameter of the preheat roller：￠900mm         预热辊直径：￠900mm

★Diameter of the angle：￠110mm×2             包角轴直径：￠110mm×2

★Steam temperature：150-200 ℃                蒸汽温度：150-200℃

★Steam pressure：0.8-1.3Mpa                   蒸汽压力：0.8-1.3Mpa

★Motor power：250W  short（S2）work system   电机功率：250W    短时（S2）工作制

4、SF-320C fingerless type single facer  SF-320C吸附式单面机

ⅰ、Structural features结构特点：

★Adopt hood suction structure，matched high pressure powerful fan. Gas supply and electrical control cabinet to focus on the same operation, the operating side full cover closed.

采用罩吸式结构，配高压强力风机。气源及电气控制集中于同一操作柜，操作侧全封闭全罩。

★High quality resin sand casting，wall thickness 200mm。Adopt independent gear box, Universal joint transmission structure.

优质树脂砂铸件，墙板厚度200mm。采用独立变速箱，万向节传动结构。

★install the lifting trolley on the conveyor bridge,Need to use the car will tile roll assembly and pressure roller, such as convenient and quick.

在输送天桥上面加装了吊装小车，需要时利用该车将瓦辊总成及压力辊等取出，方便快捷。

★Glue roller unit structure with the overall relocation，Maintenance can sway the machine at the overall maintenance，improve the working efficiency。

涂胶辊单元采用整体外移式结构，维护时可整体侧移出机处进行维护，提高了工作效率。

★The humidity control apparatus equipped with a spray, so flute type to maintain good stability of deformation, avoid dry。

配用喷雾调湿装置，使瓦楞楞型保持良好的变形稳定性，避免干裂。

★Automatic circulation system for glue, two-cylinder pneumatic gluing device, with good cushioning effect.

采用自动循环式供胶系统，双气缸气动上胶装置，具有良好的缓冲效果。

★Glue department using integrated slide structure，Glue roller surface after grinding engraved with 32 lines and pit-style textured hard chrome plating.

涂胶部采用整体式滑板结构，涂胶辊表面经精磨后刻有32线凹坑式网纹并镀硬铬处理。

★Corrugated roller adopt tungsten carbide dealing，diameter of the main corrugated roller¢ 320mm，Quenched→rough car→bore fine boring→shaft head shrunk-on→welding → tempering to stress→fine cars→coarse grinding→IF quenching→CNC grinding machine grinding→tungsten carbide dealing，hardness of surface is HV58degrees。

瓦楞辊材质48CrMo合金钢，瓦楞主辊直径¢ 320mm，经调质→粗车→内孔精镗→轴头烘装→焊接 → 回火去应力→精车→粗磨→中频淬火→数控磨床精磨→碳化钨处理。

★Active force variable frequency motor drive, energy efficient, low failure rate。

主动力采用变频电机驱动，节能高效，故障率低。

★Glue wide electric adjust to changes in the width of the paper used。

涂胶宽幅电动调整，以适应所用原纸宽度变化。

★Amount of glue size with electric adjustment, touch screen display and operation of the encoder transmission coating gap, high accuracy。

涂胶量大小采用电动调整，触摸屏显示及操作，通过编码器传输涂胶间隙，精确度高。

★Power and operating parts with a safety net to ensure the safety of personnel in the operation of machinery。

动力及操作部位配有安全防护网，以确保人员在机器运转时的安全。

ⅱ、Technical parameter技术参数：

★Effective width：1800mm                工作幅宽：1800mm

★Operation direction：left or right（determined in accordance with customer plant）

操作方向：左置或右置（根据客户厂房确定）

★Design speed：150m/min                设计速度：150m/min

★Temperature range：160—180℃         温度范围：160—180℃

★Corrugated flute:（UV type or UVV type） 瓦楞楞型（UV型或UVV型）：

ⅲ、Roller diameter parameter辊类直径参数：

★Corrugated roll diameter瓦楞辊直径： up￠313mm      down￠316mm

★Pressure roll diameter压力辊直径： ￠320mm

★Glue roller diameter涂胶辊直径： ￠240mm

★ Fixed paste roller定糊辊： ￠140mm

★Preheater diameter预热器直径： ￠402mm

ⅳ、Powered motor parameters动力电机参数：

★Main frequency drive motor：18.5KW     主变频驱动电机：18.5KW

★Suction motor：11KW                   吸风电机:11KW

★Glue reducer：100W                    调胶减速机：100W

★Glue adjusting  motor：200W*2          隔胶调整电机：200W *2

★Glue pump motor：2.2KW               胶泵电机：2.2KW

5、ZDF conveyor bridge  输送过桥

ⅰ、Structural features结构特点：

★This part is the main beam of the 20th channel, 16-beam, angle iron 63, column, etc. are connected.

本部分是主梁为20号槽钢、16号工字钢、63号角钢、立柱等连接而成。

★Both sides of the security fence, ladder , high-strength save people the word pedals, ensure the safety of personnel and easy to operate.

两侧均有安全护栏、梯子（用8号小槽钢制作）、高强度人字踏板，确保人员的工作安全以及操作方便。

★Pull the paper shaft surface tension axis, feeding shaft by grinding hard chrome plated.

牵纸轴、张紧轴、输纸轴等表面经磨削加工镀硬铬处理。

★Vacuum tension control, 5-inch suction tube, plus regulating valves, air flow can be infinitely adjustable.

真空吸附张力控制，吸风管5寸，加调节阀门，风量可无级可调。

★Dual front bezel correction guide column positioning, screw driver, fast and accurate positioning, walking steadily.

纠偏挡板前采用双导向柱定位，丝杠驱动，定位快速准确，行走平稳。

ⅱ、Roller diameter parameter辊类直径参数：

★Paper roll and a tension roller diameter:￠130mm         上纸辊及张紧辊直径：￠130mm

★Conveying roller diameter：￠180mm                    输送辊直径：￠180mm

★Active tension roller diameter：￠85mm                  主动张紧辊直径：￠85mm

★Diameter of over paper rollers and guide rollers：￠110mm 过纸辊及导纸辊直径：￠110mm

★Paper towing shaft diameter：￠110mm                  上纸拖带轴直径：￠110mm

ⅲ、Powered motor parameters动力电机参数

★Corrugated single paper lift motor：2.2KW                单面瓦楞纸提升电机：2.2KW

★The bridge adsorption motor：2.2KW                     过桥吸附风机：2.2KW

★Wide motor tune cardboard：250W                      调纸板宽幅电机：250W

6、GM-20  Glue machine涂胶机

ⅰ、Structural features结构特点：

★After the surface of cots is adjusted and tempered, the inner hole is processed, the dynamic balance surface is polished and there are 32 lines of concave net pattern, the glue is uniform and the amount of glue consumption is less.

涂胶辊表面经调质后，内孔加工，做动平衡表面精磨并刻有32线凹坑式网纹，涂胶均匀，耗胶量少。

★The rotation of the cots is controlled by the variable frequency motor and frequency conversion, and the frequency control ensures that the linear speed of the cots is synchronized with the two sides, and it can operate independently.

涂胶辊的转动由变频电机加变频控制，由变频控制保证涂胶辊的线速度与双面机同步，又可以独立运转。

★Coating electric adjustment glue amount of digital display. Automatic circulation of glue, can effectively control the amount of glue, avoid glue precipitation, ensure good glue and save glue.涂胶电动调整胶量数显。自动循环供胶，能有效控制胶量，避免胶水沉淀，保证良好的胶水和节约胶水。

★All roller surfaces are ground after hard chromium plating.

所有辊轴表面均经过磨削处理后镀硬铬。

★ The speed signal of double-sided machine is measured to realize synchronous operation with it. The rubber coating machine is displayed with man-machine interface, which can be used for data setting and easy to operate.

测取双面机速度信号，以实现与其同步运转。涂胶机采用人机界面显示，可进行相关数据设定，操作简便快捷。

★Electrical design, construction production process, follow the national standards, low failure rate, easy maintenance。

电器设计、生产施工工艺，遵循国家标准规范，故障率低，维护简单。

ⅱ、Technical parameter技术参数：

★Effective width：1800mm                         工作幅宽：1800mm

★Operation direction：left or right（determined in accordance with customer plant）

操作方向：左置或右置（根据客户厂房确定）

★Design speed：150m/min                        设计速度：150m/min

★Gas supply system：0.4—0.6Mpa                 气源系统：0.4—0.6Mpa

★Preheat cylinder temperature range：150—200℃   预热缸温度范围：150—200℃

★Steam pressure:0.8—1.2Mpa                     蒸汽压力：1.12—1.3Mpa

ⅲ、Roller diameter parameter辊类直径参数：

★Glue roller diameter：￠269mm                   涂胶辊直径：￠269mm

★Doctor roller diameter：￠142mm                 定糊辊直径：￠142mm

★Over the paper roll diameter：￠110mm            过纸辊直径：￠110mm

ⅳ、Powered motor parameters动力电机参数：

★Glue roller initiative frequency motor：3KW         涂胶辊主动电机：    3KW

★Sizing Reducer:：250W                          胶量调整减速机：    250W

★Pressure roller clearance adjustment motor： 250W 压力辊间隙调整电机：  250W

★Glue pump motor：2.2KW                        胶泵电机：2.2KW

- SM-F type double facer双面机

ⅰ、Structural features结构特点：

★The surface of the heating plate is grinded, the width of the hot plate is 600mm, there are 14heating plates, the cooling setting is 4 meters.The heating plate is made of vessel plate, which conforms to the national first-class pressure vessel standard, with pressure vessel certificate and inspection certificate.

加热板表面经研磨处理，热板宽度600mm，共12块加热板，冷却定型部长3米。加热板采用容器板制作，符合国家一类压力容器标准，附有压力容器证书及检验合格证。

★The upper conveyer belt rectifies the right and left side to adopt the pneumatic automatic correction deviation.

上输送带左右纠偏调整采用气动自动纠偏。

★Heating plate heat transfer pipe temperature control sub-four-segment, with a temperature display.  加热板的导热配管分四段控制温度，设有温度显示。

★Double cylinder S type cotton belt tensioning device is used for upper cotton belt.

上棉织带采用双气缸S型棉织带张紧装置。

★The lower belt adopts pneumatic tension, pneumatic correction.下带采用气动张紧，气动纠偏。

★Drive roller coated with attached wear-resistant rubber ，showed a herringbone structure，With a high, ensure smooth cardboard output。

驱动辊表面包附耐磨像胶，呈人字型结构，并带有中高，保证纸板平整输出。

★Main drive motor for frequency conversion motor，low-speed torque，wide speed range ,reliable, and easy maintenance.

主驱动电机为变频调速电机，低速力矩大，调速范围广，使用可靠，维护简单。

★Hot plate internal for partition isolation structure,s-shaped flow of steam，Steam, water separation function significantly improves the utilization of steam。

热板内部为隔板隔离结构，使蒸汽呈S形流向，汽、水分离功能明显，提高了蒸汽利用率。

ⅱ、Technical parameter技术参数：

★Temperature requirement：160—200℃                  温度要求：160—200℃

★Steam pressure：0.8-1.3MPa                           蒸汽压力：0.8-1.3MPa

★Air source pressure：0.6—0.9MPa                      气源压力：0.6—0.9MPa

★Cooling stereotypes length：4m                         冷却定型长度：4米

★Heating plate quantity：12 pieces                       加热板数量：12块

ⅲ、Roller diameter parameter辊类直径参数：

★Upper drive rubber roller diameter：￠700mm            上驱动胶辊直径：￠700mm

★Lower drive rubber roller diameter ：￠400mm           下驱动胶辊直径：￠400mm

★Former follower with roller diameter：￠215mm           前从动带辊直径：￠215mm

★Back setting belt driven roller diameter：￠215mm        后定型从动带辊直径：￠215mm

★Platen roller：￠70mm                                 压带辊直径：￠70mm

★Setting roller diameter：￠86mm                        定型托辊直径：￠86mm

★Upper belt tension roller diameter：￠155mm             上带张紧辊直径：￠155mm

★Upper roll diameter with detuning：￠130mm             上带调偏辊直径：￠130mm

★Entrusted with the roll diameter lower belt：￠130mm      下带托带辊直径：￠130mm

★Lower belt tension roll diameter: ￠130mm                下带张紧辊直径：￠130mm

Note: All the roller surface after grinding are hard chrome plated。

注：所有辊轴表面均为磨削后镀硬铬处理。

ⅳ、Powered motor parameters动力电机参数：

★Main drive motor power：30Kw                          主驱动电机功率：30KW

8、Slitter scorer薄刀纵切压痕机

产品概述：加轴型薄刀纵切压痕机，由于采用前后双胶计 ，大大减少对纸板长度要求，不但满足常规纸板的分切尺寸，还可以用于分切垫板等小规格纸板。电动调整分切刀和压线轮工作距离，自动锁紧，提高工作效率。

Product overview:Eight roll type slitter scorer machine,adopt two shafts in front and back of the slitter,can minimize the length of paperboard machining.Not only meet the conventional cutting board size,can also be used for cutting small cardboard pallets and other specifications.Electric adjusted the space of slitter blade,auto locking,improve the efficiency.

产品选型MACHINE CHOOSE：

|  | 产品名称 TYPE | 全电动型 Fully Electric | 宽幅（mm） WIDTH | 刀线 BLADE-SCORE | 选配 CHOOSE |
| --- | --- | --- | --- | --- | --- |
|  | SMBD | QDD | 1800 2200 2500 2800 3000 3500 3800 4000 | 4-6 5-8 6-10 7-12 8-14 例4-6代表4刀6线 | 防护网 凹形工作台 同步带传动 线型 |
| 选择（CHOOSE） | SMBD | QDD |  |  |  |

技术参数TECHNICAL INDEX：

| 型号 | Model | 2000 | 2200 | 2500 | 2800 | 3000 |
| --- | --- | --- | --- | --- | --- | --- |
| 有效分切 | Max slitting size（mm） | 1800 | 2000 | 2300 | 2600 | 2800 |
| 最小分切 | Min slitting size（mm） | 130 |
| 最小分切长度 | Min slitting length（mm） | 350 |
| 最小压线尺寸 | Min scorer width（mm） | 130 |
| 压痕高度 | Scorer height（mm） | 0-12 |
| 刀片规格 | Blade size（mm） | 200*122 |
| 刀线配置 | Blade/scorer | 4/6 ,5/8 ,6/10,7/12,8/14 |
| 尺寸 | Machine dimension | 2630*1100*1450 | 2830*1100*1450 | 3130*1100*11450 | 3430*1100*1450 | 3630*1100*1450 |
| 功率 | Power | 4.5kw | 4.5kw | 6kw | 6kw | 8kw |

电动调刀电动调线部ELECTRIC ADJUST THE SLITTER&SCORER PART：

1.电动调整分切刀工作距离，自动气动锁紧，双导轴，双锁紧气缸，运行平稳，调整方便。刀架内置聚氨酯胶圈，防尘，减少故障率。

Electric adjusted the space of slitter blade,auto pneumatic locking,Double guide optical axis,Double locking cylinder,stable operation,Convenient adjustment.The  knife rest built-in polyurethane rubber, dust prevention,reduce the failure rate.

2.电动调整压线轮工作距离，自动气动锁紧，双导轴，双锁紧气缸，运行平稳，调整方便。压线架内置聚氨酯胶圈，防尘，减少故障率。

Electric adjusted the space of slitter blade,auto pneumatic locking,Double guide optical axis,Double locking cylinder,stable operation,Convenient adjustment.The  knife rest built-in polyurethane rubber, dust prevention,reduce the failure rate.

3.压线轮气动升降，使用方便。

Under the scorer for driving wheel,six-rowed axis drive,paper smooth.

4上下压线轮同步调整，上压线轮可单独微调。

Above&lower scorer can synchronous adjustment,Above scorer can be fine-tuning

5.分切部：采用优质合金刀片，刀锋锋利，使用寿命长，分切的纸板切口整齐，无压痕，无毛刺。

Slitting part: adopt high quality tungsten steel blade, sharp and long work-life, slice more tidy, non-pressing and non-burr。

6.分纸刀前后双胶轴，最小分切长度350mm.

7.磨刀装置采用自动和手动两种气动磨刀方式，边磨刀边工作，提高工作效率

Grinding part: adopt automatic and manual two kinds pneumatic grinding type, it could be grinding when working, improve work 
efficiency

8.采用八轴设计，分切前后分别双胶轴近距离送纸，后压线成型，调整方便。可实现不压线单独分板，而且克服了后压线易跑偏现象。

Adopt eight roll , two roll-rang feeding, then scoring ,easy to ad -justment.It could be do slitting only without scoring, avoid error when scoring.

9.压痕部：采用五点压线，压痕间隙同步调整，线形美观，不爆线，易于折弯。

Scoring part: adopt 5 points scoring, scoring distance in-phase adjust, blazonry and easy to bend the carton sheet.

10.本机全部采用哈尔滨轴承，使用寿命长。

HRB bearing,long time running.

主要部件MACHINE PARTS：

| 变频器 The inverter | 中国英威腾China Inwitten | 驱动全部为英威腾品牌 All drives are inwitten brand |
| --- | --- | --- |
| 接触器，空气开关，继电器 Contactor, air switch, relay | 法国施耐德Schneider of France | 本机采用世界著名品牌施耐德 This machine adopts the world famous brand Schneider |
| 同步带 Synchronous belt | 日本 subak | 刀片旋转 The blade rotation |
| 轴承bearing | 中国哈尔滨Harbin, China | 采用著名品牌哈尔滨 Use the famous brand Harbin |
| 刀片The blade | 广东技锋刀具Guangdong jifeng cutting tools | 原生料，300万米使用寿命 Raw material, 3m service life |
| 气缸cylinder | 中国天奥 The China day | 磨刀，排单，锁紧气缸Sharpening knife, arranging single, locking cylinder |
| 电磁阀Solenoid valve | 中国天奥 The China day | 控制刀线升降，磨刀Control tool line lifting and sharpening |
| 导轨guide | 中国顺扬 China shun Yang | 底刀托 The bottom knife holder |
| 空气开关Air switch | 法国施耐德Schneider of France | 本机采用世界著名品牌施耐德This machine adopts the world famous brand Schneider |
| 按钮button | 中国正泰 China chint | 控制按钮为正泰品牌 The control button is chint brand |

9、NC-150  NC cutter helical knives  电脑螺旋刀横切机

ⅰ、Structural features结构特点：

★It can store 200 units orders，replace the cutter specifications quickly and accurately，changing orders without stop,And enables networked computers to facilitate production management.

可储存200组定单，更换切纸规格迅速准确，不停机换单，并可实现计算机联网，方便生产管理。

★Knife shaft drive gears are precision forged steel induction hardening, backlash-free transmission, advanced keyless connection, high transmission accuracy。

刀轴传动齿轮采用精锻钢材料高频淬火，实现无侧隙传动，采用先进的无键连接方式，传动精度高。

★Cutting machine adopts inlaid front steel blade knife spiral structure, serrated knife. scissors, shears, shear force, long blade life。

横切机刀片采用镶锋钢螺旋刀结构，锯齿刀型。剪刀式剪切，剪切力小，刀片寿命长。

★Around feed rollers are used  the sun gear platen way, smooth delivery, pressure evenly, easy to crush plate board or cause blockage。

前后送纸轮均采用太阳轮压纸方式，输送平稳，压力均匀，不易压坏板板或造成堵塞。

★This type of brake is energy storage type (non-energy brake), so in the process of production, the average power consumption is 1 / 3 of that of the ordinary NC cutting machine, saving more than 70% of electricity and achieving the goal of saving money.

本机型是储能式制动（非能耗制动），故在生产过程中低能耗，平均用电量是普通NC切断机的1/3，节省电70%以上，达到省钱的目标。

★Exact and adjustable no gap gear to ensure precise blade engagement, running balance.

精密可调无隙齿轮，确保刀口精确啮合，运行平衡。

★Independent oil pump and filter are used to distribute two sets of copper pipes in each gear position to feed oil, lubricate and cool.

采用独立油泵和过滤器配合两组紫铜管分布于各齿轮位供油，润滑和冷却。

★Knife roller: fine quality forged steel material, the balanced, with good stability.

刀辊：优质精锻钢材质，经平衡处理，具有良好的平稳性。

ⅱ、Technical parameter技术参数：

★Effective width：1800mm                          工作幅宽：1800mm

★Operation direction：left or right（determined in accordance with customer plant）

操作方向：左置或右置（根据客户厂房确定）

★Design speed: 150 m / min                         设计速度：150m/min

★Mechanical configuration: computer helical cutter crosscutting  机械配置：电脑螺旋刀横切

★Minimum cutting length：500mm                    最小切纸长度：500mm

★Maximum cutting length：9999mm                  最大切纸长度：9999mm

★Cutter accuracy: Uniform for ± 1mm,  non-uniform to ± 2mm

切纸精度：匀速为±1mm，非匀速为±2mm

★Equipment size: Lmx4.2 Wmx1.2 Hmx1.4            设备尺寸：Lmx4.2*Wmx1.2*Hmx1.4

★Single machine weight: maximum 3500kg            单机重量：最大3500Kg

ⅲ、Roller diameter parameter辊类直径参数：

★Cross on the knife shaft center distance：￠216mm    横切上、下刀轴中心距：￠216mm

★Before the lower conveying roller diameter  ￠156mm  前下输送辊直径  ￠156mm

★After the lower conveying roller diameter：￠156mm   后下输送辊直径：      ￠156mm

★Roll diameter: 160mm。                            牵纸辊直径：￠160mm

★Output solar wheel diameter: 160mm                 输出太阳轮直径： ￠160mm

Note: all roller shafts after grinding, the surface of hard chromium plating (except upper, lower tool shaft).

注：所有辊轴均经磨削后，表面镀硬铬处（上、下刀轴除外）理。

ⅳ、Powered motor parameters动力电机参数：

★main drive motor power：22Kw   Full AC synchronous servo

主驱动电机功率：22KW             全交流同步伺服

★Before feeding motor power：3Kw（Frequency Control）

前后输纸电机功率：3KW（变频调速）

10、DMT-120paper sheet delivery and side conveyor直角堆码机

ⅰ、Structural features结构特点：

★Adopted on the 16th channel welded。Electric adjustment of cardboard the size of the lateral output pneumatic control board, electrically adjustable conveyor speed.

采用16号槽钢焊接。电动调整纸板尺寸，气动控制横向输出纸板，输送速度电动可调。

★Cardboard sheets to the desired number or height requirements will be controlled by a foot switch out of cardboard。

纸板张数或高度至所需要求时由脚踏开关控制将纸板移出。

★Vertical bin using wide flat belt conveyor transport。

纵接纸采用宽幅输送平带输送。

ⅱ、Technical parameter技术参数：

★The maximum accumulation length：3000mm  最大堆积长度：3000mm

★The maximum stack height：200mm          最大堆积高度：200mm

ⅲ、Powered motor parameters动力电机参数：

★Main conveyor motor：3Kw   adopt frequency motor

主输送电机：3KW             采用变频电机

★Lateral output of the motor：1.5Kw    Three-phase asynchronous motor

横向输出电机：1.5KW                  三相异步电动机

★Walking Motor：1.5Kw    Three-phase asynchronous motor

行走电机：1.5KW           三相异步电动机

11、ZJZ glue station system   制胶站系统

ⅰ、Structural features结构特点：

★Provide the starch adhesive to the corrugated single facer , glue machine and some other gluing equipment.

为单面瓦楞机，涂胶机等用胶设备提供淀粉粘合剂。

★Horizontal glue machine can meanwhile matched  with main body glue and carrier glue, and mixing, glue large。

卧式制胶机可同时配制主体胶和载体胶，并混合搅拌，制胶量大。

★Making room storage barrels adhesive solution was to use the glue pump rubber equipment storage barrels, adhesive solution for equipment。

制胶房储存桶胶液被胶泵输送到各个用胶设备的储存桶里，为设备提供胶液。

★Storage barrels, plastic barrels with mixing device, avoid glue solution precipitation agglomerate。

储存桶、供胶桶自带搅拌装置，避免胶液沉淀结块。

★System unit with carrier vessel, main tank, storage tank, and send the glue pump, the back glue

pump, etc。制胶装置分别有载体罐，主体罐，贮存罐，及送胶泵、回胶泵等组成。

★Glue system adopt glue cycle,rest glue go back to the glue square cylinder,Liquid level float automatic control,the back glue a bucket of glue liquid being beaten back with glue equipment storage bucket，cycle for glue，Save the glue solution，prevent the glue solution in the rubber plate pasting and caking precipitation.

制胶系统采用循环供胶，余胶流到回胶方桶里，液位浮球自动控制，回胶方桶里的胶液被打回到用胶设备的储存桶里，进行循环供胶，节约胶液，防止胶液在胶盘中糊化和结块沉淀。

★Work has been completed, the residual gum dividend total pipeline with rubber equipment rubber pumped back rubber room storage barrels, for next time use。

工作完毕后，各用胶设备余胶被除数总管道胶泵抽回胶房储存桶里，供下次使用。

★Responsible for technical guidance, teaching adhesive dispensing process。

负责技术指导，传授粘合剂配制工艺。

ⅱ、Technical parameter技术参数：

★Horizontal body glue mixer：one                   卧式主体胶搅拌机： 1台

★Carrier glue mixer：one                           载体胶搅拌机：1台

★Storage glue mixer：one                          储存胶搅拌机：1台

★Plastic buckets on coater：one                    涂胶机上胶桶：1件

★Coating machine back plastic buckets :one        涂胶机回胶桶：1件

★Plastic buckets on single machine :two              单面机上胶桶：2件

★Single machine back plastic buckets：two           单面机回胶桶：2件

★Lose glue dispensing pumps：four                  输胶胶泵：4台

ⅲ、Glue barrel diameter parameters胶筒直径参数：

★Horizontal body glue mixer：1250mm×1000mm×900mm

卧式主体胶搅拌机：1250mm×1000mm×900mm

★Carrier glue mixer  diameter：  ￠800mm×900mm

载体胶搅拌机直径：￠800mm×900mm

★Diameter plastic bucket on Glue：￠800mm×1000mm

涂胶上胶桶直径：￠800mm×1000mm

★Plastic buckets on single machine：￠800mm×1000mm

单面机上胶桶：￠800mm×1000mm

★Storage tank diameter：￠1200mm×1200mm

储存胶桶直径：￠1200mm×1200mm

ⅳ、Powered motor parameters动力电机参数：

★Horizontal body glue mixer：3Kw                          卧式主体胶搅拌机：3KW

★Carrier glue mixer：2.2Kw(Ordinary three-phase)            载体胶搅拌机：2.2KW(普通三相)

★Output plastic pump motor ：2.2Kw（Ordinary three-phase） 输胶泵电机：2.2KW（普通三相）

★Storage Tank Motor：1.5Kw（Ordinary three-phase）        储存胶桶电机：1.5KW（普通三相）

12、ZQ steam system蒸汽系统

ⅰ、Structural features结构特点：

★Production line for hot heating energy delivery device to maintain a stable operating temperature。为生产线各用热设备输送加热能源，保持工作温度的稳定。

★All units are designed to be independent small unit for the steam system, segmented temperature control, energy saving, easy to adjust。

各机组均设计成独立小单元供汽系统，分段控温，节约能源，调整方便。

★By adjusting the steam pressure monitor dial to exercise control over the operating temperature, and a pressure。

通过调节蒸汽压力实行对工作温度的控制，并设有压力监视表盘。

★Each group has a hydrophobic unit emptying bypass, when rapid shutdown cooling equipment。每组疏水单元均设有排空旁通，停产时设备降温迅速。

★Float trap 1/2 metal hose and connect the bypass valve, plug valve injection。

倒桶疏水器，不锈钢止回阀，不锈钢芯截止阀门。

★Between the piping system and the rotary heating member in order to achieve a flexible metal hose connection, to extend the service life of the rotary joint。

管道系统与旋转加热部件间以金属软管实现柔性连接，以延长旋转接头的使用寿命。

★All steam pipes are made of seamless steel tubes, to ensure safety for use under normal pressure。

所有机内蒸汽管道均选用无缝钢管，确保正常压力作用下使用的安全性。

ⅱ、Technical parameter技术参数：

★Steam consumption: about 2.5-3T/h          蒸汽耗量：约2.5-3T/h

★Equipped with boiler：4t/h                   配用热源：4t/h

★Equipped with boiler pressure：1.25MPa   Pipe temperature：170—200℃

蒸汽压力：1.25Mpa       管道内温度：170—200℃

※Main parts, raw materials, origin (brand)

主要部件、原材料、产地（品牌）

| Name of main parts 主要件名称 | Brands or place of origin 品牌或产地 | Material 材质 |
| --- | --- | --- |
| Main motor 主电机 | Hebei hengshui 河北衡水 |  |
| Reducer 减速机 | Shandong, De zhou,Jin zhan 山东德州金展 |  |
| Bearing 轴承 | HRB、ZWZ、CYC 哈、瓦、洛 |  |
| Seat belt bearing 带座轴承 | Zhengjiang five rings 浙江五环 |  |
| Contactor, relay 接触器、继电器 | France Schneider 法国施耐德 |  |
| Paper clip head 夹纸头 | Xusheng 旭升 | 3 inches and 4 inches in common 3英寸、4英寸共用 |
| Steam rotary joint 蒸汽旋转接头 | Shandong Quanzhou Yujie 山东泉州玉杰 |  |
| Preheating 预热缸 | Hangang or Jigang 邯钢或济钢 | Q235Bpressure vesselplate Q235B压力容器板 |
| Trap 疏水阀 | Beijing 北京 | Floating ball type 浮球式 |
| Wallboards and bases 墙板及底座 | Self birth 自产 | HT200 |
| Air cylinder 气缸 | Zhejiang Sanzheng 浙江三正 |  |
| Heating appliance 加热板 | Tiangang or Jigang 天钢或济钢 | Fabrication of Q235B Container Plate Q235B容器板制作 |
| Cotton tape 棉织带 | Shenyang 沈阳 | Thickness 10mm 厚度 10mm |
| hydraulic pressure station 液压站 | Hebei 河北 |  |
| photoelectric switch 光电开关 | South Korea Autonics 韩国Autonics（奥托尼克斯） |  |
| electromagnetic valve 电磁阀 | Adriatic 亚德客 |  |
| Belt 同步带 | Germany OPTIBELT 德国奥比 |  |
| Tensioning sleeve 涨紧套 | Xianyang chaoyue 咸阳超越 |  |
| proximity switch 接近开关 | OMRON, Japan 日本欧姆龙OMRON |  |
| Flying shear servo control system飞剪伺服控制系统 | Germany Kobe 德国科比 |  |
| Motion control board 运动控制板 | Germany 德国MKS-CT150 |  |
| Touch screen 触摸屏 | Kunlun tongtai 昆仑通态 |  |
| Sun wheel 太阳轮 | Shenzhen China 中国深圳产 |  |
| Inverter、PLC 变频器、PLC | Taiwan Delta 台湾台达 |  |
| pneumatic component 气动元件 | Adriatic 台湾亚德客 |  |